## Slide 1
Limiting Instabilities in Multibunch : Review and Cures
Alban Mosnier, CEA/DAPNIA - Saclay
Since very high beam currents are distributed among many tightly spaced bunches unstable coupling between bunches through long-range wakefields has become the main limiting instability
Conventional Coupled-bunch mainly driven by :
long-range parasitic modes of rf cavities
resistive wall (transverse)
New recently discovered collective effects :
fast ion instability (for e- rings)
photo-electron instability (for e+ rings)

## Slide 2
Energy & position oscillations spoil :
Luminosity in colliders (wrong time/position collisions)
Brilliance in SLS (undulators strongly sensitive to increase in effective beam energy spread or emittance)
Ex. effect of a coupled-bunch longitudinal instability on the brightness of a typical undulator in the SOLEIL Light Source

## Slide 3
General theory for multi-bunch instabilities exists for more than 20 years
(Sacherer '73, Pellegrini & Sands '77, …)
Rigid bunch approximation (Coherent motion of bunch as a whole)
 stability of the system = eigenvalue problem
 Single-particle equation of longitudinal motion :
 for M equally spaced and equally populated rigid bunches,
coherent oscillation of the k-th bunch described by
 Signals add up coherently (synchrotron sidebands) with
 total induced voltage = sum of the currents of the M individual bunches
Impedance sampled at frequencies

## Slide 4
For evenly filled rings  analytical expression
well-know coherent frequency shift
and growth rate
Zeff = aliasing of Z//() into the band from 0 to M0
Transverse coupled-bunch instabilities (very similar)
For unevenly filled rings  eigenvalues of a MM coupling matrix (K. Thompson & R. Ruth '89, S. Prabhakar '00)
Prabhakar : more convenient to expand the uneven-fill modes into the set of the M basis vectors formed by the even-fill modes proposed modulation coupling of strong even-full modes to alleviate CBI

## Slide 5
CBI growth rate strongly dependent on fill pattern (observed at various storage rings, ex. APS '97)
Main idea : • for each unstable mode n corresponds an highly stabilised counterpart m = M-n • create then a coupling of unstable modes to stable modes through uneven fills • find the best current distribution among the RF buckets which minimises the largest instability growth rate
Simplest case : 1 HOM and its effective impedance with uniform filling M = h buckets = 396 • couple the unstable mode (n=165) to the stable mode (m=231) by uneven filling (same I0) ex. only every Nth bucket is filled so that (m-n) ≈ M / N ( max. coupling ) N=6 but demands that HOM frequencies be well controlled ex. freq shift excite next mode n=164

## Slide 6
Usual Cures against Coupled-Bunch Instabilities
attempts to
Landau damping  destroy the coherence of the beam
HOM frequency control  avoid the overlap of HOMs with beam spectrum
Heavy mode damping  reduce the resonant buildup of fields (grapples directly with the source)
Active feedback  apply a correction signal from a sensed error signal

## Slide 8
Landau Damping
successfully used for the operation at ESRF
When oscillators (either particles in a bunch or different bunches in the train) have a finite spectrum of natural frequency
 net beam response to the driving force due to WFs 
beam stable again if frequency spread large enough.
 Dispersion Relation
Coherent frequency shift
w/o Landau & radiation damping

## Slide 9
 rf voltage modulation
easily provided by beam loading in the rf cavity with partial filling
frequency distribution ≈ rectangular spectrum
for phase modulation  total spread
At ESRF : instability threshold increased
from ≈ 60 mA  beyond nominal intensity of 200 mA with a 1/3 filling
SOLEIL :
2/3 filling
100 mA

## Slide 10
Stability diagram for the SOLEIL ring
assuming 352 MHz LEP Cu cavities 1st HOM at ≈ 500 MHz (R/Q=75, Q=3.104)
 radiation damping only + HOM with 16 mA
 rectangular spectrum (spread = 6.3 %) + HOM with 100 mA.
But frequency spread of only 0.3 % for 2/3 filling and 100 mA
 method impractical for the SOLEIL ring
plot in complex plane : - locus of the inverse of the integral as  is swept from - to + - frequency shift w/o Landau and radiation dampings (HOM frequency, not exactly known, also scanned  0 looks like resoannce curve of the HOM

## Slide 11
Bunch-to-bunch frequency splitting
can also be achieved by driving the normal RF cavities at a frequency (h±1) f0
 used at CERN to suppress longitudinal instability in PS ('71)  tested at ESRF by driving 2 of the 4 installed cavities at one revolution harmonic above the rf frequency
n=1 instability prevents cavities from being tuned close to h+1 rev. Harmonic  tradeoff between modulation level & reflected power  170 mA max

## Slide 12
 Landau Cavity
non-linearities in focusing force  some spread in synchrotron frequency Max. Freq. spread in bunchlengthening mode: slope total voltage ≈ 0 at bunch loc
Quartic bucket potential
maximum generally much lower than natural synchrotron frequency
Ex. SOLEIL freq. Spread of 200%, But center-freq. dramatically decreased  net result = poor improvement
 radiation damping only + HOM with 16 mA  spread from 3rd harm. cav. + HOM with 18 mA.

## Slide 13
 Betatron spread (transverse plane)
significant spread easily obtained :  non-linearities in the focusing system  with non-zero chromaticity, together with energy spread   multi-bunch instability after // instability on most existing rings (crude threshold calculation gives the inverse)
With Gaussian distribution in energy
stability recovered for rms betatron freq. spread
Ex. SOLEIL with LEP Cu cavities 1st deflecting HOM fr=614 MHZ R/Q=360 /m Q=6.104
current threshold ≈ 6 mA  240 mA with  = 0.1 E /E <10-3

## Slide 14
HOM Frequency Control
CB modes spaced one revolution frequency apart  some latitude to escape HOMs from beam spectrum lines small rings & HOMs not damped
developed and routinely used at ELETTRA : HOM tuning by precise cavity temperature control
Procedure :  find temperature settings which give largest stability windows for all cavities  refine by direct measurement of CBM spectrum on the machine
Frequency of cavity mode k
Temperature Fundamental tuning = F(beam current)

## Slide 15
But difficulty to find temperature intervals stable for both longitudinal and transverse planes  movable plungers designed at ELETTRA for allowing additional degree of freedom
W/o plunger after plunger adjustment
long.
trans.
6 ELETTRA-type cavities in SOLEIL
5 MV rf voltage and 400 kW rf power
No stability intervals for 25% ( over 100 different seeds )

## Slide 16
Heavy Mode Damping
cavity modes damped as much as possible to lower the resonant buildup of fields 2 technologies SC & NC developed to meet high power & low impedance challenges
SC advantages :  fewer cells  lower overall impedance for given voltage due to the high CW gradient capability  higher achievable deQing large beam holes allowed, while keeping very high Rs HOMs propagate out & easily damped  Mode Damping used alone for SC cavities used with feedback system for NC cavities
SC drawbacks :  larger complexity (cryogenics)  precautions against risk of cavity & coupler pollution

## Slide 17
 Normalconducting cavities
Dampers mounted directly on cavity walls at proper locations (max. coupling)
HOM power carried out & dissipated on external rf loads Waveguide couplers : cut-off frequency ≥ fundamental mode frequency  natural FM rejection & higher deQing than coaxial couplers 3 ridged waveguides generally placed symetrically around the cell  additional power dissipation, due to field penetration into the waveguide
Ex. DANE cavity
includes 2 additional WGs

## Slide 18
 Superconducting cavities
Dampers cannot be directly mounted on the cavity walls (risk of multipactor, magnetic quench and surface contamination)
But; beam tubes made large enough for efficient coupling to the cavity modes
2 approaches :
 Dampers = beam pipes themselves (CESR, KEK-B) rf lossy material (ferrite) to the inner surface of both pipes, outside the cyostat
 More classical HOM dampers mounted on beam pipes in the vicinity of the cavity (LHC, SOLEIL)
 needs large openings to ensure the propagation of all modes with high HOM powers  outgassing rate of ferrite (surface contamination)
 more challenges on HOM couplers (power & de-Qing) optimized in combination with string of cavities

## Slide 19
cryostat of KEK-B SC cavity
Wide beam pipe & closer iris ( modes) coaxial high power input coupler ferrite HOM loads
cryostat of CESR SC cavity
fluted beam pipe ( modes) WG high power input coupler ferrite HOM loads

## Slide 20
accelerating mode
longitudinal HOM
Ex. Cavity-pair arrangement for SOLEIL
Features : weak coupling for the accelerating mode & strong coupling for HOMs

## Slide 21: Coupler optimization with RF codes

## Slide 22: Results of calculation (2 couplers / cavity) Highest impedance (at optimal coupler location) versus inner tube length and for different tube radii Conclusion : diameter of 400 mm and cavity spacing ≈ 3/2 seem optimal Fundamental mode : R/Q = 45  / cavity Epeak/Eacc = 2 Hpeak / Eacc = 4.2 mT/(MV/m)

## Slide 23
Tuning system
(180 kHz/mm
resolution ≈ 50 nm)
Cryo transfer lines phase separator
Power coupler
(200 kW)
He tank
HOM couplers
352 MHz Nb/Cu cavity
Vacuum tank
Conduction break
4°K  300°K
schematic drawing of the SOLEIL cryostat developed within the framework of a collaboration with CERN

## Slide 24
Assembly & Power tests at CERN
Eacc > 7 MV/m Qo > 109
main coupler Pinc = 160 kW w/o beam
static losses = 20 W @ 4°K

## Slide 25
Feedback Systems
Developed for more than 20 years
 first in frequency domain, on a mode-by-mode basis (Ex. CERN PS booster)  more recently in time domain, on a bunch-by-bunch basis thanks to the advent of commercially available fast DSPs
complementary to passive mode damping can damp definitely all coupled bunch modes impedances arising from strong HOMs first sufficiently reduced correction kick voltage needed :
Ex. 1st HOM of 2 LEP Cu cavities in SOLEIL ring Full coupling  84 kV / turn (assuming mode amplitude 1.5°) required power > 5 MW !!!

## Slide 26
Model Driving term = correction kick
FB loop gain (V/rad) Delay time
Complex frequency shift
 / 2 for G > 0 Max. damping : phase shift 3 / 2 for G < 0

## Slide 27
 mode-by-mode feedback for only a few troublesome coupled-bunch modes
 bunch-by-bunch feedback for a large number of bunches
bunches treated as individual oscillators minimum bandwidth = half the bunch frequency
PEP-II, ALS, DANE, etc… : common longitudinal feedback system design based on fast ADC/DAC converters & DSP chips for digital filtering
 digitizing of the baseband error signal
 N-taps FIR : max. gain at fs + zero dc response
 Downsampling (low fs)
 Efficient diagnostics tool : measurements of growth & damping rates by means of time domain transient techniques

## Slide 28
Resistive Wall Instability About the required BW of a transverse feedback
Resistive wall impedance
 only modes with spectrum lines close to the origin, will be excited
 feedback system with limited bandwidth (few revolution harmonics) generally sufficient averaged measurements over several bunches
for high current rings, with large number of bunches
 many coupled-bunch modes are unstable at zero chromaticity
 > 0 : m=0 mode stable
But  not too large :
 transverse dynamic acceptance spoiling
 emergence of higher order head-tail modes

## Slide 29
growth rates of head-tail modes (+ higher order radial modes) easily evaluated by solving the Sacherer’s integral
Ex. SOLEIL RING growth time of most unstable modes vs. chromaticity number of unstable modes for the first 3 head-tail modes
Conclusion : transverse feedback of, typically, a few tens of MHz bandwidth with a proper chromaticity setting (not too large to avoid head-tail modes, but large enough to reduce the number of unstable rigid bunch modes m=0 )

## Slide 30
fast ion instability (for e- rings)
Analog as single-pass BBU in Linacs, except coupling between bunches due to ions intead of wakefields
Linear theory : displacement
gas ionization rate per unit length
But with ion frequency spread around ring : exp. growth and
Not very severe for usual gas pressure
easily cured by fast feedback or Landau damping (induced by octupoles / choma)
photo-electron instability (for e+ rings)
CBI instability caused by photo-electrons created by SR at pipe wall (Ohmi)
Coupling between bunches due to primary e- (interaction with several bunches before hitting the opposite wall) or due to electron cloud buildup in steady-sate
Cures e- cloud dominated : TiN coating (secondary e- yield  reduction ex.PEP-II) primary photo-e- : magnetic field to maintain e- far from beam (KEK-B)