## Slide 1
Microwave Instability : Importance of impedance model
Alban Mosnier, CEA/DAPNIA - Saclay
In modern rings,lot of precautions are taken :
 vacuum join + rf contact used for flanges  screening of vacuum ports
 shielding of bellows
 very smooth tapers ...
 vacuum chamber impedance tends to be more inductive Z/n << 1 
But …  High frequency tail of rf cavity impedance
 Trapped modes produced by slots, BPMs … (enlargements of beam pipe)
 resonances

## Slide 2
Ex. Effects of the tapered transitions of the SOLEIL cavity
Wakes induced by a 4 mm long bunch  large broadband resonance ≈ 11 GHz
Problem : Tracking codes require the knowledge of the point-like wake at very short distance s (≈ 1 order of magnitude smaller than bunchlength  a few tenths of mm) while time-domain wakefield codes provide bunch wakes for finite bunchlengths ex. unreasonable to consider z< 1 mm for SOLEIL structure of total length 5 m ! Solution : Point-like wake can be inferred from a fit of lossfactors computed for ≠ z

## Slide 3
Evolution of the relative rms bunchlength and energy spreads
current linearly increased from 0 to 50 mA flat-top at 10000 turns
Results of tracking simulations …
chamber impedance modelled by cavities + tapers only
 Ith ≈ 40 mA
similar result by using a 11 GHz broadband resonator
Initial (Gaussian) and final charge densities
Bunch more populated at head due to resistive character of impedance

## Slide 4
With the aim to investigate the effect of BB impedance center-frequency
Vlasov-Sacherer approach combined with the “step function technique” for the expansion of the radial function, as proposed by Oide & Yokoya ('90)

 provides a better insight into the involved instability mechanisms than tracking simulations
 takes into account the spread in synchrotron frequency, which plays a primary role in the instability onset (due to potential well distortion by wakefields and eventual harmonic cavity)
 keeps all terms of the Vlasov equation (no “fast growth” approximation)
 Gets a handle on the existence of several bunchlets created by the stationnary wakefield (case of low frequency resonator)
 Gives threshold prediction in good agreement with time-domain simulations

## Slide 5
For illustration: SOLEIL storage ring + broadband resonator
High Resonant Frequency (30 GHz) potential well distortion …
Charge distributions for ≠ currents synchrotron frequency vs action variable

## Slide 6
Low Resonant Frequency (11 GHz) potential well distortion …
bunch more distorted than before with 2 peaks above 3.5 mA, as soon as there are two or more stable fixed points, forming distinct islands

## Slide 7
Re & Im coherent frequency vs current
 complete mixing at relatively low current after a rapid spread
 growth rate increases dramatically ≈ 5 mA (= onset of the instability)
 several types of instability (identified by solid circles) develope simultaneously
 the nature of the most unstable modes changes with the intensity :
above threshold (5 mA) microwave instability mainly driven by coupling of dipole and quadrupole modes;
instabilities finally overtaken by the radial m=5 mode coupling above 8 mA;
High frequency : Stability of the stationnary distribution …

## Slide 8
 growth rate looks more chaotic than before, because of the rapid change of the topology of the phase space, (emergence of two or more bunchlets)
 weak instabilities below 4 mA ( growth rate close to radiation damping rate)
 above 4 mA (which can be considered as a threshold) two mode families with regular increase of the growth rate (identified by solid circles)
 sudden change of behaviour at 6 mA
Low frequency : Stability of the stationnary distribution …

## Slide 9
In short,
Whatever the nature of the instability (radial or azimuthal mode coupling) is
and despite a large azimuthal mode number range
(from m=1 or 2 at low frequency to m=5 or 6 at high frequency),
the onset of the instability doesn't depend a lot on the resonator frequency
However,
 Threshold is not the only criterion
 generally, lower frequency resonators are more harmful : induce dipole or quadrupole oscillations of large amplitude
 In addition, sawtooth type instabilities can develop, owing to the formation of micro-bunches.
threshold current vs norm. frequency r

## Slide 10
Saw-tooth instability :
a possible trigger
Tracking results :
 sudden outbreak at 6 mA
 quick increase of both energy spread and bunch length,
 followed by a slower decrease, with recurrence of about 150 Hz.
density-plot of the most unstable mode,
calculated from Vlasov-Sacherer (6 mA) :
 azimuthal pattern : reveals a pure dipole mode inside the tail bunchlet
 this unstable dipole mode widens so far as to reach the separatrix of the tail island
 particles can diffuse through the unstable fixed point and populate the head bunchlet, leading to relaxation oscillations

## Slide 11
Harmonic Cavity
Primary goal of an harmonic cavity = to increase beam lifetime in SLS
(operating in the bunchlengthening mode)
Side-effect : push up the microwave instability
Energy gain :
Induced voltage : (idle cavity)
For example, effect of an harmonic cavity on the microwave instability, driven a broadband resonator of center frequency 20 GHz
(fundamental cavity + additional harmonic cavity only) k= 0.328
external focusing nearly zero around bunch center  z increased by a factor 3

## Slide 12
Strong reduction of the peak current  large reduction of the instability is expected
Besides, multiple bunchlets are suppressed (final voltage, including wake potential smoothed off)
However, even though particle density divided by a factor of about 4 instability threshold multiplied by a factor 2 only
Efficiency loss explanation : lower synchrotron frequency spread due to lower potential well distortion
In case of short bunches, the non-linearity (even operating at 3rd harmonic) and then the Landau damping effect much smaller than w/o harmonic cavity

## Slide 13
Vlasov-Sacherer method tracking results
bunches much longer  modes of higher azimuthal periodicity easily excited Different modes (quad., sext., …) at center and at periphery of the bunch
Density-plots of the distributions of the most unstable three modes - 15 mA -