## Slide 1: 3 rd Libera Users Meeting 22th of June 2009
Libera Software status at the ESRF
F.Epaud
3rd Libera Users Meeting /22th of June 2009 /F.Epaud-Software Engineering Group

## Slide 2: 4 Liberas devices for Bunch by Bunch Feedback
LiberaAccess TANGO device server (Access to the FAI and DDRAM)
MultibunchFeedback TANGO device server
Java application for operation (on left)
FPGA program developed by I-TECH, F.Uberto (Transverse), G.Gautier (Longitudinal)
LabVIEW application for ‘Experts’ (below) [Courtesy of G.Gautier]
Currently extended to make Tune measurement
 Problem since the upgrade with the DDRAM buffer
3rd Libera Users Meeting /22th of June 2009 /F.Epaud-Software Engineering Group
Libera BBFP
(Vertical)
LiberaAccess
MultiBunchFeed
Libera BBFP
(Longitidinal)
LiberaAccess
MultiBunchFeed
Libera BBFP
(Horizontal)
LiberaAccess
MultiBunchFeed
Pick up
stripline
Pick up
Kicker
Kicker
Kicker
Pick up
stripline

## Slide 3: 1 Libera device for Transfer Efficiencies measurement
1 Libera Electron + FPGA ESRF’s design (Graham Naylor) for the Transfer Efficiencies measurement:
  4 striplines (TL1, SY, TL2, SR) connected to the ADC inputs of the Libera
  FPGA program makes measurement on 16 programmable windows delayed from T0 or Text
  LiberaAccess TANGO device server (Access to the FAI and DDRAM)
  XfrEffLibera TANGO device server:
    Set-up the system
    Acquires raw data
    Calculates charge, efficiencies and SR/SY phase,
    Bufferize results during injection
    Store to HDB offline
  Java application
3rd Libera Users Meeting /22th of June 2009 /F.Epaud-Software Engineering Group
Libera Electron
LiberaAccess
XfrEffLibera
4 Pick up
Striplines
TL1, SY, TL2, SR
HDB
T0, Text,
In Injection

## Slide 4: 3 Liberas brilliance for TL2 BPM
3 Liberas Brilliance for TL2 BPM
  BPMLibera TANGO device server from SOLEIL
  LiberaPulsedBPM
  Java application
3rd Libera Users Meeting /22th of June 2009 /F.Epaud-Software Engineering Group
Libera
(Brilliance)
BPMLibera
Libera
(Brilliance)
Libera
(Brilliance)
BPMLibera
LiberaPulsedBPM
Pick up
Pick up
BPMLibera
LiberaPulsedBPM
LiberaPulsedBPM
Pick up

## Slide 5: 224 Liberas brilliance for SR_BPM
3rd Libera Users Meeting /22th of June 2009 /F.Epaud-Software Engineering Group
SR-BPM ( 224 devices = 32 cells with 7 BPMs)
ESRF uses V1.82 (on ~5 Cells ) and V2.02 + V2.03 patch (on ~27 Cells)
One TANGO device server per Libera
Still using the ”old” version (1.1.6) of Soleil server with ESRF’s modifications:
    Arctan positions algorithm
    SAsum Threshold
    X and Z Global offsets
    Incoherency calculation
    Others small modifications ….
“New” version of Soleil server in test:
    Taken from CVS repository (CVS version 1.1.11)
    Re-included ESRF’s modifications mentioned above
    Port to Libera version V2.02 (+V2.03 patch) without the new functionalities
    Added new ESRF Modifications:
      X and Z Global offsets re-implemented in a better way to handle FOFB
      Removed memorized attributes and use a Global property for setting
      Added calculation of RMS on DD buffer
      Latter: Add calculation of Lifetime
    Will make a new CVS branch
    Will include soon some of the V2.02 new functionalities: PM decimation, Antispike, …

## Slide 6: BPMLiberaAll TANGO device server
Run on top of the 224 BPMLibera device servers
Functionalities:
    Internal thread running at 2Hz to collect the X, Z positions and status from all the Liberas
      Uses TANGO group calls (15 mS to read one plan)
      Build an History buffer of 3 minutes for SA Xpos, SA ZPos and SA Sum
      Problem: Can not read 2D attributes (image), therefore 3 calls are necessary and we can’t assume that we read the same sample (~20 mS delay between calls)
    Generates events to be used by the clients
    Correct data according to beam current
    Store data to HDB (soon as 1D vector): Positions, RMS, Va, Vb, Vc, Vd, Temp, Fan Speeds
    Read/Set Parameters to all Liberas (e.g. OffsetTune, DDEnable, DDDecimation, DDBufferSize, …)
    Checks incoherent setting of parameters
    Checks BPM head incoherencies
    Permanently reset the BPI interlocks when the SR current is below 6 mA.
Improvements:
    Detection of frozen Libera
    Handling of Trigger for Turn by turn and FOFB (New hardware in development)
3rd Libera Users Meeting /22th of June 2009 /F.Epaud-Software Engineering Group

## Slide 7: Applications (1)
SRCO: Slow Orbit Correction (X11 application):
    Previous application modified to handle new Libera BPM system
    During the smooth upgrade from the old system, this application handled the 2 types of BPM:
      First it tries to read the Libera BPM
      If no Libera was there it read the old BPM
X and Z positions MAP display (java application):
    Wait for events (@2Hz) and rebuild and display the Positions history
3rd Libera Users Meeting /22th of June 2009 /F.Epaud-Software Engineering Group

## Slide 8: Applications (2)
Post Mortem Analysis (java application)
  In specification
COD: (dumb terminal application):
  Analysis of beam motions during gap change
  Libera system drastically speeded-up the analysis
  Used only during MDT shifts only
Libera BPM Manager (LABView):
  Display the 224 statuses
  Display X and Z SA positions (corrected or not)
  Allows to access one Libera and see ADC, DD or SA data
  Display the incoherencies of crucial parameters
  Allows to display the chosen parameters on the 224 Liberas
3rd Libera Users Meeting /22th of June 2009 /F.Epaud-Software Engineering Group

## Slide 9: SR-BPM Computing architecture
Problem to connect to the previous network architecture: Need to be in auto-negotiation
 speed-up the already planned network upgrade
32 cells with 7 BPMs each (224 Liberas)
-> One dedicated VLAN (not physically dedicated network, shared with the rest of the control)
4 last generation Linux crates (new version: PCI Express, Pentium 4 Core Duo /2 GHz – 3MB RAM (56 devices servers on each of them)
1 dedicated computer to run BPMLiberaAll
Computing resources needed per BPMLibera TANGO device server. Measured with SRCO application @1Hz
Mode | % CPU (server) | % Network 100 Mbs
SA | 6% (~0.1 %) | 
SA + DD (5.5K samples + Decim = 64, 1Hz trigger) | 20 % (~0.4%) | 
3rd Libera Users Meeting /22th of June 2009 /F.Epaud-Software Engineering Group

## Slide 10: Fast Orbit Feedback (FOFB)
Uses the CC (Communication Controller) developed by DLS and now integrated as an option within the Libera
Uses the ESRF’s network infrastructure (4 pairs out of 12 coming from the 32 cells to the Electronics room behind the control room)
3 cells out of the 32 (Cells 1,2,3) are wired and communicates together
Sniffer:
. Same FPGA card as Soleil (vmetro) [PMC + PCI carrier]
. Actually uses the FPGA code developed by Soleil
. Soleil’s Sniffer device server installed on Windows XP (not Vista)
. Vmetro Linux driver debugged and ported to Linux/redhate4 (but with kernel regeneration)
. Connected to Cell 1
. Positions from the 3 wired cells can be acquired
Synchronization:
. Very difficult at the moment:
- No control of the trigger (uses a generator to manually send single pulse)
- Uses ‘ssh’ to all (21 at the moments) Libera to set the time and start the CC
- Needs to stop the TANGO devices servers before doing the ‘ssh’ otherwise an error is returned from the CSPI
. New trigger electronics in development  new device server to write
. BPMLibera should be modified in order to start the CC (set_time is already implemented)
3rd Libera Users Meeting /22th of June 2009 /F.Epaud-Software Engineering Group

## Slide 11: To DO
Libera firmware upgrade(s):
    Finish the upgrade of 5 Cells + 6 BPI stations from V1.82 to V2.02 (+V2.03 patch)
    Upgrade all to V2.04
BPMLibera device server:
    Complete the test of the ‘new’ version
    Install it
    Include V2.02 features
    Include ESRF’s FOFB needs: start CC,
BPMLiberaAll device server
    Detect frozen Libera
    Trigger clock management.
    ……
FOFB:
    Finish the wiring and commissioning of the Communication Controller
    Trigger box device server
    Steerers power supplies device server
    Certainly a device server to control the FOFB embedded control within the FPGA
3rd Libera Users Meeting /22th of June 2009 /F.Epaud-Software Engineering Group