## Slide 1: ESRF Fast Orbit Feedback Upgrade
ESRF Accelerator & Sources Division JM Koch
<number>
Key elements of the system
Sequencing
Topology
Material involved
Latency
Planning
Notes: <number>
Introduction….. Project FOFB Eric Plouviez.
With this new version of the FOFB, we will have better control of the beam position at all locations in the storage ring. So first I will recall the key elements of this improvement, then I will describe the sequencing of the loop, the proposed topology, the material involved, then the latency we have to face in this loop and I will conclude with the planning for its implementation.

## Slide 2: ESRF Fast Orbit Feedback
ESRF Accelerator & Sources Division JM Koch
<number>
Fast Orbit Feedback improvement
 Key elements of the system
96 Horizontal & Vertical steerers
housed in the sextupoles
224 Libera BPMs
One unique system to cover the full frequency range
Notes: <number>
The major improvement of this version will be the use of the 224 Libera BPMs for the acquisition of the beam position and the use of the 96 Horizontal & Vertical steerers at all the frequencies covered by the system to cancel the beam motion.

## Slide 3: ESRF Fast Orbit Feedback
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
Fast Orbit Feedback sequencing
Ethernet
-----
-----
One of the 8 Feedback Processors
One of the 96 sextupoles housing the correctors
Group of 7 Liberas per cell
4 cabinets of 18 corrector’s channels each
One of the 224 Beam Position Monitors
 1: Beam position acquisition on 224 Libera BPMs
7 Liberas
In each of
the 32 cells
Notes: <number>
I now come to the sequencing of the loop, the cycle of the loop is about 100us
The sequence starts with the acquisition of the positions by all the Liberas simultaneously.
This represents the BPMs, one group of 7 Liberas in each of the 32 cells, 8 Feedback Processors, the corrector power supplies and the sextupoles.

## Slide 4
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
Fast Orbit Feedback sequencing
Ethernet
-----
-----
 2: All positions exchanged between Liberas…
One of the 8 Feedback Processors
One of the 96 sextupoles housing the correctors
Group of 7 Libera BPMs per cell
4 cabinets of 18 corrector’s channels each
One of the 224 Beam Position Monitors
ESRF Fast Orbit Feedback
…and transferred to signal processors
Notes: <number>
…then the exchange of the data through a dedicated network between all the Liberas…

## Slide 5
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
Fast Orbit Feedback sequencing
Ethernet
-----
-----
 3: Corrections computation on 8 stations (FPGAs)
One of the 8 Feedback Processors
One of the 96 sextupoles housing the correctors
Group of 7 Libera BPMs per cell
4 cabinets of 18 corrector’s channels each
One of the 224 Beam Position Monitors
ESRF Fast Orbit Feedback
Notes: <number>
…the corrections are then computed in these processors…

## Slide 6
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
Fast Orbit Feedback sequencing
-----
-----
Ethernet
 4: Corrections transferred to Power Converters
One of the 8 Feedback Processors
One of the 96 sextupoles housing the correctors
Group of 7 Libera BPMs per cell
4 cabinets of 18 corrector’s channels each
One of the 224 Beam Position Monitors
ESRF Fast Orbit Feedback
Notes: <number>
…and the results sent to the power supplies.

## Slide 7
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
Fast Orbit Feedback sequencing
-----
-----
Ethernet
 5: Current sent to the correctors…
One of the 8 Feedback Processors
One of the 96 sextupoles housing the correctors
Group of 7 Libera BPMs per cell
4 cabinets of 18 corrector’s channels each
One of the 224 Beam Position Monitors
… and corrections applied to the beam
ESRF Fast Orbit Feedback
Notes: <number>
…to update their setpoints and the current feeding of the steerers…

## Slide 8
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
Fast Orbit Feedback sequencing
-----
-----
Ethernet
One of the 8 Feedback Processors
One of the 96 sextupoles housing the correctors
Group of 7 Libera BPMs per cell
4 cabinets of 18 corrector’s channels each
One of the 224 Beam Position Monitors
 5: Current sent to the correctors…
… and corrections applied to the beam
ESRF Fast Orbit Feedback
Notes: <number>
…the corrections are applied to the beam in both planes simultaneously.
As you can see in this representation, the corrections are located in four different places. The choice of these locations was governed by the existing cabling of the steerers:
The processing devices will be installed close to the power supplies to minimize the amount of cabling.
<CLICK>
At each of these 4 locations we have :
The power supplies
Two processing devices
The links to the closest cluster of Liberas

## Slide 9
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
Rocket IO
Rocket IO
BPM
BPM
BPM
BPM
BPM
BPM
Topology (1/4 of the machine)
Cell+n
Cell+m
BPMs of 1 cell over 8 and correctors scheme for 1/4th of the machine (SRDC location example)
---
BPM
BPM
Cell-n
Cell-m
PMC Feedback Processor DSP-1
18 RS485
Correctors Power Supplies
6 H&V  18 ch
24 RS485
Correctors Power Supplies
8 H&V  24 ch
18 RS485
Correctors Power Supplies
6 H&V  18 ch
21 RS485
Correctors Power Supplies
7 H&V  21 ch
PMC Feedback Processor DSP-2
C
P
U
E
t
h
PMC Feedback Processor DSP-1
PMC Feedback Processor DSP-2
 Data from digital B.P.M.s
ESRF Fast Orbit Feedback
Notes: <number>
2 Liberas are connected to each processor to ensure a redundancy of the data transfer.
<CLICK>
The link is made with the nearest? group of Liberas.

## Slide 10
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
Material involved  Digital B.P.M. Libera Brilliance
Acquisition:
224 H & V positions from Libera BPMs grouped by cells (7/cell)
Position data rate for fast orbit feedback: 10kHz
There are 2 kinds of communication channels:
Configuration,
slow rate monitoring
Ethernet
Fast Communication
for data exchange at 10kHz
RocketIOs
Fast communication: copper for the very short links inside one rack and optic fiber for the inter-cells connections 
Libera Brilliance. Set-up for one cell
ESRF Fast Orbit Feedback
Notes: <number>
As already mentioned, the Liberas are grouped by 7 units, which is the number of BPMs per cell.
There are 2 kinds of communication channels on the Liberas:
_ one for the configuration and slow rate monitoring through Ethernet
_ and the so called « RocketIOs » for fast communication that will be used for the FOFB.
The connections will be made with copper for the very short links inside one rack and with optic fibers for the inter-cell connections.

## Slide 11
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
 10kHz communication network
Libera Brilliance and Digital Signal Processors communication network is redundant
The full exchange of 224 positions H & V will take 50µs even if a connection is broken
Topology
Communication Controller from Diamond Light Source:
“ Every 100µs, each BPM injects its own beam position values to the FOFB network, and then starts a forwarding or discarding process on the BPM values that it receives.
Each BPM position then propagates to all 224 BPMs and the 8 processing modules on the network before the end of the time frame.“
ESRF Fast Orbit Feedback
Notes: <number>
… to create this network we will make use of the existing fibers already installed between the cells and the control room.
All the Libera groups will be connected to the control room and from there, will be connected between themselves
The communication controller has been developed for the FOFB of the Diamond Light Source and is being used by Soleil as well.
Every 100µs, each BPM injects its own beam position values to the FOFB network, and then starts a forwarding or discarding process on the BPM values that it receives. Each BPM position then propagates to all 224 BPMs and the 8 processing modules on the network before the end of the time frame.
This works even if a link is broken, thanks to the redundancy of this topology.
Field Size Description
Header 32 Bit BPM ID, Source type, TimeFrameStart
x-Position 32 Bit x-Position of the beam [nm]
y-Position 32 Bit y-Position of the beam [nm]
Reserved 32 Bit Reserved
Time Stamp 32 Bit Time stamp of position data acquisition [ns]
The Liberas are synchronized and start sending the positions all at the same time.
The processing modules are synchronized by the “Time Frame Start” bit embedded in the packet header.

## Slide 12
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
Topology (1/4 of the machine)
PMC Feedback Processor DSP-1
Rocket IO
18 RS485
Correctors Power Supplies
6 H&V  18 ch
24 RS485
Correctors Power Supplies
8 H&V  24 ch
18 RS485
Correctors Power Supplies
6 H&V  18 ch
21 RS485
Correctors Power Supplies
7 H&V  21 ch
PMC Feedback Processor DSP-2
Rocket IO
C
P
U
E
t
h
PMC Feedback Processor DSP-1
PMC Feedback Processor DSP-2
 Digital Signal Processing
BPM
BPM
BPM
BPM
BPM
BPM
Cell+n
Cell+m
BPMs of 1 cell over 8 and correctors scheme for 1/4th of the machine (SRDC location example)
---
BPM
BPM
Cell-n
Cell-m
ESRF Fast Orbit Feedback
Notes: <number>
Once all the data has been received by the processing devices, the corrections are computed and the results sent to the power supplies (twisted pair cables), let’s now have a look at these processing devices…

## Slide 13
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
Material involved
Commercial card in a PCI, same behaviour than Libera (Embedded Diamond L.S. Communication Controller):
  As communication node and signal processor, the FPGA will embed the signal processing
   Real time inside the FPGA
  For diagnostic purposes or transfer of parameters through the PCI interface
   Not real time
 PMC module (Gbit Ethernet + Virtex-II FPGA)
ESRF Fast Orbit Feedback
Notes: <number>
This is a module with four optical links holding an FPGA which is the same as in the Libera which collects the data of all the positions and is connected on 2 Liberas in one cell, it is used :
  As communication node and signal processor, the FPGA will embed the signal processing :
  the real time is done inside the FPGA
  For diagnostic purposes or transfer of parameters through the PCI interface :
  this part is not in real time

## Slide 14
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
Material involved
Digital Signal Processing:
  Multiplication by the inverted response matrix,
  Digital P.I. correction,
  RS485 Power Converters command.
On an FPGA the computation can be split on many channels running in parallel, the time for computation can be estimated for one channel only:
  One compromise between FPGA area occupation and speed can lead to :
  224 multiplications + sum, this gives a total of about 300 cycles of the FPGA less than 3µs
 PMC module (Gbit Ethernet + Virtex-II FPGA)
ESRF Fast Orbit Feedback
Notes: <number>
The processing of the data is composed of 3 parts:
The multiplication of each position vector with the corresponding vector from the inverse response matrix,
the processing of the corrections,
the output of the setpoints toward…

## Slide 15
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
Topology (1/4 of the machine)
PMC Feedback Processor DSP-1
Rocket IO
18 RS485
Correctors
DC Power Supplies
6 H&V  18 ch
24 RS485
Correctors
DC Power Supplies
8 H&V  24 ch
18 RS485
Correctors
DC Power Supplies
6 H&V  18 ch
21 RS485
Correctors
DC Power Supplies
7 H&V  21 ch
PMC Feedback Processor DSP-2
Rocket IO
C
P
U
E
t
h
BPM
BPM
BPM
BPM
BPM
BPM
Cell+n
Cell+m
---
BPM
BPM
Cell-n
Cell-m
BPMs of 1 cell over 8 and correctors scheme for 1/4th of the machine (SRDC location example)
 Steerers Power Supplies
AC/DC PS units
AC/DC PS units
AC/DC PS units
AC/DC PS units
ESRF Fast Orbit Feedback
Notes: <number>
… the 3 channels of the power supply required for each vertical and horizontal correction.
The present DC power supplies will be replaced by New <CLICK> units …

## Slide 16
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
Material involved
Correction:
Steerers: 96 Horizontal & Vertical
Power supplies: 3*96 channels able to drive up to +/- 2 Amp DC and small currents up to 200Hz (+/- 17 bits resolution)
288 channels located in 18 cubicles grouped by ¼ of the machine in the technical gallery.
¼ of the steerers DC Power Converters to be replaced by AC-DC Power Converters
The correctors are part of the sextupoles (6 black coils)
The corrections will be applied at the acquisition rate, each 100µs.
A prototype of AC power supply has been validated in real situation.
ESRF Fast Orbit Feedback
Notes: <number>
…able to drive small AC corrections in the steerers on top of the 2 Amp DC current.
The 288 channels are located in 18 cubicles grouped by 1/4th of the machine, in the technical gallery inside the storage ring.
The corrections will be applied every 100µs

## Slide 17
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
Critical inside the 100 µs time frame
* Data from Diamond Light Source
** Inside the 8 dedicated FPGAs
Libera
ESRF Fast Orbit Feedback latency
Group delay of FIR: 148 µs
Group delay of 2 IIR: <71 µs
Distribution of data around the ring (DLS C.C.): 50 µs *
Signal processing: 10 µs **
Write into PS controller: 20 µs
Power supply: 70 µs
Eddy currents in the sextupoles: 75 µs
Eddy currents in vacuum chamber (stainless-steel): 265 µs
. .
Total: <709 µs
ESRF Fast Orbit Feedback
Notes: <number>
One important figure regarding the performances of the FOFB is the delay in the loop:
First of all the processing in the Libera, some 200µs, then the distribution of the data around the storage ring, the computation of the corrections, the transfer to the power converters, the response time of these power converters to drive the required current and at the end of this chain, the eddy currents in the magnets and in the stainless steel vacuum chambers, the most important figure with 265 µs (we measured this latency for the aluminium chambers as well and it is almost twice this value, some 600 µs, which is why we have to stick on the stainless steel chambers solution).
We were quite surprised to note that the eddy currents in the yoke of the sextupoles did not cause as much delay as compared to the value induced by the vacuum chambers.

## Slide 18
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
ESRF Fast Orbit Feedback implementation planning
Optic fibers for the dedicated network March 2009
Communication Controller on Liberas and one PMC-FPGA processor Spring 2009
AC Power Converter prototype validation Spring 2009
Server for multi-turns diagnostics Summer 2009
AC Power Converters installed for DC corrections only (Remote access through Ethernet) fast correction based on air coil correctors remains active 2010
Implementation of the fast orbit correction on 8 PMC-FPGA processors End 2010
ESRF Fast Orbit Feedback
Notes: <number>
As regards the planning, this has started with the ordering of a prototype of the power supplies, the laying of optic fibers which will be completed very soon now when all the Liberas will be inter-connected.
The first tests will concern the communication controller, the development of the server for the multi-turns diagnostic will be ready later on, the prototype of the power supplies has been tested as well. If everything goes well, these power supplies will be installed in 2010 for DC corrections only at first, the implementation of the full AC correction will hopefully be ready by the end of 2010.

## Slide 19
ESRF Accelerator & Sources Division JM Koch
<number>
07/28/26
Acknowledgements
Nicolas Hubert (Soleil)
Nicolas Leclerc (Soleil)
Michael Abbott (Diamond Light Source)
Tony Dobbing (Diamond Light Source)
Gunther Rheim (Diamond Light Source)
Isa Uzun (Diamond Light Source)
Francis Epaud (ESRF)
Eric Plouviez (ESRF)
ESRF Computing service
ESRF Diagnostic group
ESRF Power Supply group
Thank you for your attention !
ESRF Fast Orbit Feedback
Notes: <number>
To conclude, I would like to thank people with whom I am regularly in touch for this project, people from the ESRF of course but also from Soleil and Diamond from whom we obtained the main elements of this topology.