## Slide 1
Libera Workshop 2008
Peter Leban, Andrej Košiček
Libera Brilliance, Recent Patches, new Ideas, Future
peter.leban@i-tech.si
Grenoble, June 22nd 2009

## Slide 2
Release 2.00 issued in December 2008
Current patch release 2.04, sent out last week
MAIN FEATURES |  | 
Release 2.00 | Release 2.02 | Release 2.03/2.04
Upgrade to armel platform Considerably faster floating point operation Use of NPTL (Native Posix Threading Library) Using pipes for passing events instead of signals - Improved DHCP functionality FPGA/SBC throughput increased by cca 30% Programmable PM triggering Spike Removal on TbT, FA and SA data Position calculation from ADC rate buffer (single pass, CW) | Bugfixes PM buffer with d64 data Faster AGC (@~1Hz) Integration of DLS Communication Controller | - Bugfixes
Libera Brilliance/Electron Current Status

## Slide 3
2.20 Propositions:
Access to DSC Coefficients
Proposed By: | Description / Benefits
ESRF/Instrumentation Technologies | If a component in the analog chain fails (behind analog switch), the measurement is still valid if the DSC (switching) is on. This is because the input signals are all rotated through all channels. This can result in slight position offset and slightly increased RMS. Such status can be effectively diagnosed by monitoring the DSC (amplitude compensation) coefficients.

## Slide 4
2.20 Propositions:
Beam life-time Measurements
Proposed By: | Description / Benefits
ESRF | Libera Brilliance has a potential to rival standard current monitors in speed & stability . The other advantage is that there are lots of Liberas around the ring, allowing better statistics. Life-time measurement is based on the decay of the averaged SA-Sum signal (over certain period of time).

## Slide 5
2.20 Propositions:
Standard & MAF Designs Together
Proposed By: | Description / Benefits
ESRF | Possibility to have the Standard & the MAF design installed on memory inside each Libera. to load the desired design into FPGA by a local script possibly no need to restart Tango (or other control system) device-servers after a design change.

## Slide 6
2.20 Propositions:
Bypass Notch when DSC (switching) off
Proposed By: | Description / Benefits
NSLS2 | The Notch filter in FA data chain is inserted to suppress the lower switching harmonic. If DSC is off, the Notch is not needed. Could be usable for testing purposes since during normal operation DSC should be on.

## Slide 7
2.20 Propositions:
ADC Offset Compensation
Proposed By: | Description / Benefits
NSLS2 | The goal is to achieve better accuracy for single pass position measurement from ADC rate buffer, especially at lower ADC counts. Feature does not need any additional runtime parameter. Simple calculation (here for channel A): ChA_offset=mean(channelA); channelA=channelA-ChA_offset;

## Slide 8
2.20 Propositions:
Timestamp on SA Data
Proposed By: | Description / Benefits
NSLS2 | To include timestamp in SA data as an additional column. This should be a counter which is reset with set-time trigger.

## Slide 9
2.20 Propositions:
ADC Underflow Checking
Proposed (and Ordered) By: | Description / Benefits
ESRF | The goal is to prevent unnecessary Interlock triggering when the beam is lost. The algorithm checks the amplitude on all 4 channels If the level is below predefined limits (e.g. 700 counts on 16bit ADCs) on all channels, the Interlock is not triggered.

## Slide 10
2.20 Propositions:
Statistics calculation inside Libera
Proposed By: | Description / Benefits
ESRF | The calculation of RMS and mean value on DD and SA data. Check the beam’s AC stability The goal is to reduce the amount of data transfer through internal network and further calculation in the servers. User would define the number of samples for calculation. Calculation for position and amplitudes.

## Slide 11
Future of Libera Brilliance (dreaming…)
Possible scenarios | Purpose | Change
The Release 2.20 | Constantly upgrading with new functionalities | SW
Graphical User Interface (GUI); independent of Epics and Tango (?) | To help new users, on-click parameter settings, on-click acquisitions | SW
Upgraded Libera Brilliance: bigger FPGA | To provide more space for FPGA software programming | HW
Libera Brilliance on the new platform | Completely new platform with new software, the new instrument generation; using same principles for data processing | HW, SW

## Slide 12
Thank you for your attention.