## Slide 1
15th ESLS-RF Workshop, ESRF, Grenoble, France
October 5-6, 2011

## Slide 2
OUTLINE
  FERMI@Elettra Overview:
    Machine description
    Commissioning results
  S-band RF System:
    RF transmitters
    Waveguides
    Accelerating structures
    SLED phase modulation
    LLRF
  Outlook

## Slide 3
FERMI@ELETTRA
OVERVIEW

## Slide 4
 50 m
Experim. Hall
 100 m
Undulator Hall
 200 m
Linac Tunnel +
Injector Extension
FERMI at the ELETTRA LABORATORY
Elettra Synchrotron Light Source
FERMI@Elettra FEL

## Slide 5
FEL1
FEL2
I/O mirrors & gas cells
PADReS
EIS
DIPROI
LDM
Photon Beam Lines
slits
experimental hall
undulator hall
Transfer Line
FEL1
FEL2
L1
X-band
BC1
L2
L3
L4
BC2
linac tunnel
PI
Laser Heater
MACHINE LAYOUT
FERMI@Elettra is a Single-Pass, 50 Hz, Seeded FEL facility covering the wavelength range from 100 nm (12 eV) down to 4 nm (320 eV)
FERMI is based on a warm 1.5 GeV linac.
The accelerator consists of a new high-brightness electron source, a laser heater system for the control of uncorrelated energy spread, a 4th harmonic accelerating section to linearize the bunch charge, and two magnetic bunch compressors to increase the delivered peak current.

## Slide 6
DESIGN GOALS & ACHIEVEMENTS
2008 | 2009 1-6 |  | 2009 7-12 |  | 2010 1-6 | 2010 7-12 | 2011 1-6 |  | 2011 7-12
Design |  |  |  |  |  |  |  |  | 
 |  | Construction |  |  |  |  |  |  | 
 |  |  |  | Commissioning |  |  |  |  | FEL2 tests
 |  |  |  |  |  |  |  | FEL1 Operations | 
Parameter | FEL1 | FEL2 | Units
Output Wavelength (fund.) | 100 – 40 | 40 – 10 | nm
Peak Power | 1 – 5 | > 0.3 | GW
Repetition Rate | 10 | 50 | Hz
Energy | 1.2 | 1.5 | GeV
Peak Current (core) | 200 – 800 | 800 | A
Bunch Length (fhwm) | 0.7 – 1.2 | 0.7 | ps
Slice Norm. Emittance | 1.5 – 3.0 | 1.0 | mm mrad
Slice Energy Spread | 0.20 | 0.15 | MeV

e
* achieved
FEL2 final design
Lasing
Buildings
Users
FIRST
LASING
Infrastructures on time
FEL2 Design Completion
Civil Engineering and Installations
Machine Upgrades
RF Condition. and FELI Commissioning
FELI Operation
Light to Beam Lines
Parameter | FEL1 | FEL2 | Units
Output Wavelength (fund.) | 100 – 20 | 40 – 10 (4) | nm
Peak Power | 1 – 5 | > 0.3 | GW
Repetition Rate | 10 | 50 | Hz
Energy | 1.2 | 1.5 | GeV
Peak Current (core) | 200 – 800 | 800 | A
Bunch Length (fhwm) | 0.7 – 1.2 | 0.7 | ps
Slice Norm. Emittance | 1.5 – 3.0 | 1.0 | mm mrad
Slice Energy Spread | 0.20 | 0.15 | MeV

## Slide 7
S-BAND RF SYSTEM

## Slide 8
GENERAL
Fifteen RF plants (fourteen plus a spare one).
Eighteen accelerating structures.
Waveguide system to provide power to the structures, RF gun and deflectors.
Low Level RF for all the plants.

## Slide 9
STATUS
  RF TRANSMITTERS:
    Fourteen RF transmitters operational.
    Spare transmitter to be completed by the end of the year.
    Transmitters operating at 10 Hz, upgrade to 50 Hz in 2012.
  ACCELERATING STRUCTURES:
    Sixteen accelerating structures in operation.
    Two to be acquired.
    SLED systems operational.
  LOW LEVEL RF:
    All plants equipped with intermediate LLRF.
    Final system construction in progress.

## Slide 10
RF TRANSMITTERS
Klystron TH 2132A-typical parameters | 
Frequency | 2998 MHz
Peak RF power | 45 MW
RF pulse width | 4.5 µsec
Pulse repetition frequency | 10-50 Hz
Gain at full output power | ≥ 53 dB
Efficiency in saturation condition | ≥ 43%
Beam cathode voltage (typical) | 310 kV
Peak cathode current | 350 A
PFN Modulators – typical parameters | 
Maximum output voltage | 320 kV
Maximum delivered current | 350 A
Repetition frequency | 10-50 Hz
RF pulse width | 4.5 µsec
Risetime / falltime | < 2 µsec
Pulse flatness | < ± 1%

## Slide 11
RF TRANSMITTERS PERFORMANCE
Transmitters are in operation on a 24 hours/day basis.
After clearing the early faults, the main issue is the still high number of what we call “peak I faults”, i.e. an anomalous increase in the klystron current:
  They account for more than 90% of the total faults on the S-band System.
    They are generally random distributed and resettable.
    They are power dependent.
Specific actions were taken to improve the situation:
  Klystron heating curve optimization.
  Klystron HV conditioning.
  Studies on peak current threshold definition.
  Optimization of operating levels after putting into operation the SLEDs.
Klystron | Beam current (% of I max) | RF power
K1 | 61 % | 21 MW
K2 | 83 % | 33 MW
K3 to K7 (typ) | 81 % | 33 MW
K8 to K14 (typ) | 66 % | 24 MW

## Slide 12
RF TRANSMITTERS PERFORMANCE
Results:
  Fault/day/mod: decrease to less than 0.9, however still higher that what should be expected for the operating levels, according to Thales.
  Global uptime of the system increased to more than 90 %, which is acceptable for the time being but we are working to improve it.
Next actions:
  Start a testing program using either K15 or K0 to analyze modulator performance to look if there is any other part of the system which could affect the arc rate.
  Perform HV conditioning during shutdowns or in case of fault rate increase.
  Routinely perform filament optimization (effect on the lifetime of the tube).

## Slide 13
RF POWER DISTRIBUTION
Two main RF power distribution schemes are used:
    One klystron feeding two sections.
    One klystron feeding a single high gradient accelerating structures equipped with SLED system.
  OFHC WR284 waveguides working either under ultra high vacuum or under SF6 pressure.
  Waveguide attenuators and phase shifters are used to control in phase and amplitude the power in case of multiple users.
  An array of switches is used to connect the spare system in case of need to replace one of the first two klystrons.

## Slide 14
ACCELERATING STRUCTURES (1)
There are four types of accelerating structures:
S0a and S0b:
    3.2 m. long
    constant gradient, TW
    2/3π mode, on-axis coupled
    From old Elettra injector
C1 to C7:
    4.5 m. long
    constant gradient, TW
    2/3π mode, on-axis coupled
    From CERN after LIL decommissioning

## Slide 15
ACCELERATING STRUCTURES (2)
There are four types of accelerating structures:
S1 to S7:
    6.15 m. long
    constant impedance, BTW
    3/4π mode, magnetically coupled
    From old Elettra injector
    Equipped with SLED
Two more structures to be acquired and installed:
    They will replace the first two sections (S0a and S0b) that will be eventually relocated along the machine.
    The new structures will have to minimize phase and amplitude asymmetries in the coupler cells, to minimize the induced kick to the beam.
    3.2 m. long.
    constant gradient, TW.
    2/3π mode, on-axis coupled.
    Call for tender to be launched in the next months.

## Slide 16
ACCELERATING STRUCTURES PERFORMANCES
All available structures in operation.
No new issue.
SLED operational and implemented phase modulation.
Energy Budget:
Type | Number | 1.2 GeV | 1.5 GeV | 1.5 GeV
Gun | 1 | 5 MeV | 5 MeV | 5 MeV
S0a-S0b | 2 | 47.8 MeV | 47.8 MeV | 47.8 MeV
C1-C7 | 7 | 57 MeV | 57 MeV | 57 MeV
S1-S7 | 7 | 110 MeV | 150MeV | 136 MeV
New sections | 2 | // | // | 50 MeV
Total Energy |  | 1270 MeV | 1550 MeV | 1552 MeV
Typical power from the klystron will not exceed 35 MW.
The energy required for FEL-2, i.e. 1.5 GeV, should be attained with a reasonable margin for availability and reliability.

## Slide 17
SLED PHASE MODULATION
During the operation of the BTW structures as injector for Elettra the very high field built up due to conventional SLED operation prevented from reaching the expected gradient.
Phase modulation operation mode for the SLED systems can help to lower the very high peak field inhered with conventional operation and make it flatter, so it can help to overcome this limitation and to reach the goal of an energy gain of more than 150 MeV.
Phase modulation feature was implemented in the LLRF firmware.
Phase Modulation paybacks:
    Reduce number of breakdown events due to high peak field in the structures.
    Allows elongating RF pulse.
    Rise the energy gain for each structure.
Reached 165 MeV energy gain on the structure used for the tests.

## Slide 18
LOW LEVEL RF
Specification on amplitude and phase stability: 0.1 % and 0.1° at 3 GHz.
The LLRF is an all-digital system.
One chassis per accelerating structure.
The two main boards were developed specifically for FERMI:
  RF front end board:
    Five RF inputs and two RF outputs.
    Performs frequency conversion between RF (3 GHz) and IF (99 MHz) and hosts all the frequency dependent components.
  Digital processing board (AD board):
    Virtex5 FPGA with 2 Gbytes on board RAM.
    Performs all controls diagnostic and external communication.
System developed in the frame of a collaboration agreement between Sincrotrone Trieste and Lawrence Berkeley National Lab.
Due to the delays in the construction of the AD board, an “intermediate” system has been installed, where the so-called LLRF4 boards are used. Chassis designed for direct replacement between the two boards.
This solution allows to perform the basic functionalities, although the ultimate performances can be attained only with the new boards.

## Slide 19
LOW LEVEL RF
Intermediate system performance:
    All loops needed have been implemented on the intermediate system:
      Loops: amplitude, phase, cable calibration and phase locking loop.
      SLED: phase reversal and phase modulation.
    Specification on amplitude and phase stability reached.
    Issues: tuning problems.
    The system is very crucial for the reaching of the performance of the beam needed for the FEL.
Final system:
    Prototype board fully tested on bench and on the machine with beam.
    Firmware ported from LLRF4 board to the final board.
    Pre-series board in test.

## Slide 20
OUTLOOK

## Slide 21
NEXT STEPS
Raise machine energy to 1.5 GeV in 2012 for FEL-2.
RF power plants:
    Complete spare plant, which is needed to test the 50 Hz RF gun in Spring 2012.
    Upgrade plants to 50 Hz operation.
    Improve performance.
  Accelerating Structures:
    Complete conditioning of all BTW structure to maximum power.
    Procurement of the two additional structures.
  LLRF:
    Complete AD boards construction.
    Upgrade chassis to final systems.
    Install of slave controller for dual cavity plant.
    Firmware development.

## Slide 22
FUTURE DEVELOPMENTS
  LLRF firmware:
    Short term:
      Real time communication between master and slave AD boards and loops development.
      Intrapulse feedback loop.
      Reflected power interlocks implementation through LLRF.
    Long term:
      Study connection of LLRF controllers through high speed serial links to a central controller (Matrix card, developed at CERN/Los Alamos):
        Global communication with the control system.
        High bandwidth communication between LLRF controllers or other diagnostics.
      Integration of LLRF and link stabilizer firmware (if required).
      Investigate iterative learning possibilities.
  Investigate upgrade path for the system both in terms of power increase and reliability aspects.

## Slide 23
ACKNOWLEDGEMENTS
I would like to thank:
My colleagues of the S-band RF system team:
    Paolo Delgiusto, Federico Gelmetti, Massimo Milloch, Andrea Milocco, Federico Pribaz, Angela Salom Sarrasqueta, Claudio Serpico, Nicola Sodomaco, Rocco Umer, Luca Veljak, Defa Wang.
  Our collaborators for the LLRF construction and development.
  Simone Di Mitri and Michele Svandrlik for providing material for this presentation.
  The FERMI Commissioning Team and all the people involved in the commissioning for the results on the machine.

## Slide 24
THANK YOU FOR YOUR ATTENTION