## Slide 1: Monitoring the length of the bunches in the ESRF storage ring using microwave cavity pick ups

## Slide 2: Principle of the diagnostic
If we assume (but it is wrong) that the longitudinal bunch profile is a Gaussian, we can derive the bunch length value from the measurement of the current spectrum at only two frequencies f0 anf f1
Let us take f0 =0 and lets us be clever with the choice of f1

## Slide 4: S(f) current spectral density
30GHz full span
Purple: multibunch
Blue:16bunches
16GHz
10GHz

## Slide 5: Microwave pick-up signal processing (RF front end)
RF combiner
BP filter
352.2 MHz RF clock
X28 multiplier
10.2GHz
cavity
10.2GHz
cavity
352.2 MHz signal
->Libera Brillance
Frequency down conversion for easier signal processing
Pill box cavity
Cavity axis
Ceramic iris

## Slide 6: Pick ups set up
Ceramic iris

## Slide 7: RF front end set up

## Slide 8: Microwave pick-up signal processing : 352.2 MHz demodulation in a Libera
Signal level normalization using a Libera Brillance
Libera Brillance

cavity signal frequency downconverted to 352.2MHz
BPM pick ups
attenuator
Same RF levels for the reference bunch length

## Slide 9: Bunch length derivation from the Libera output data
S is the spectrum of the current s(t) of a unit charge Gaussian bunch of FWHM =2.35
Ln(S()/S0mA()) = -1/220mA2
S(S(mA) = -1/20mA
for two different bunch lengths 0mA and with0mA
If <<
This why we work at 10GHz instead of 16GHz …
S(S(mA) is given by the Libera …

## Slide 10: Test results
Bunch length variation caused by a change of the RF amplitude, monitored using the streak camera and the microwave signal monitor;
I =32mA, stored in 992 bunches
Vertical: Libera data
Horizontal: Streak camera data

## Slide 11: Test results
Bunch length variation caused by a change of the RF amplitude, monitored using the streak camera and the microwave signal monitor;
I =32mA, stored in 32 bunches
Vertical: Libera data
Horizontal: Streak camera data

## Slide 12: Exemple of measurements
50ms full span
15KHz full span
.5ps
16 bunch filling, 65 mA (end of decay)
fs related lines

## Slide 13: Exemple of measurements
50ms full span
2ps
15KHz full span
fs related lines
?
16 bunch filling, 85 mA (just after the refill)
A very different pattern…

## Slide 14: Exemple of measurement
Bunch length spectrum evolution during a 5 hours decay from 90 to 70 mA
20KHz span

## Slide 15: Data logging

## Slide 16: Conclusion
It is a nice addition to the streak camera:
Data always available without any tuning (for permanent data logging)
High data rate available
Sub picosecond resolution
But:
Requires an initial calibration using a streak camera
Does not give any information on the bunch shape
Remark:
instead of a cavity pick up, a strip line followed by narrow bandwidth band pass filters could probably work as well..