## Slide 1
Z. Martí, U. Iriso
Accelerator Division, CELLS
May 2014
Beam Energy Measurements through Spin Depolarization at ALBA

## Slide 2
Introduction: the recipe
Inject a fresh beam up to a beam current whose lifetime is limited by Touscheck
Wait until beam gets polarized (anti-parallel to the dipole Bfield), noticeable because lifetime increases
Scan a vertical excitation at a frequency around expected energy resonant tune. When the vertical excitation is in resonance with the spin tune, and beam gets depolarised
When the beam is depolarised, the beam gets a sudden loss, producing:
        lifetime drops
        beam losses increase
        Product (DCCT * lifetime) decays

## Slide 3
Excitation Hardware
Arbitrary Function Generator - AFG3102
100W Amplifiers
Fast Feedback Kickers: Zsh = 45 kOhms
Kick: 0.67urad (7 uT·m)
ALBA | Soleil | SLS | Diamond
7uT m | 4.8uT m | 3.5uT m | 45uT m
Kick numbers comparison with other labs (numbers for IPAC references)

## Slide 4
Measurement Hardware
Lifetime (or product) DCCT
Lifetime (or product) using BPMs Sum signal
1 Scintillator based loss monitor (Beam Loss Detector – BLD)
120 PinDiodes Bergoz Beam Loss Monitors (BLM)
Keees BLD
BLD Location in the Ring:
Downstream Hor and Ver Scraper
Both are slightly closed to increase losses at this location

## Slide 5
Results: Polarization
First, polarization build up is confirmed.
For this case, BPMs fans and gains shall be fixed.

## Slide 6
Scaning the excitation frequency with steps up to 5Hz/s, no lifetime drop is observed.
Instead some strange peaks appear in the lifetime.
Suspected Qy-Qx, but moving the tunes the peaks do not move consistenty.
First Results: frequency scans

## Slide 7
Peaks study – changin WP

## Slide 8
Full scan: [0 – 0.5]
The result is that we are full of peaks!!
Even if we change the WP, we still get peaks here and there
Ver beam size evolution (blue) during the freq scan

## Slide 9
Zoom on peaks
Example: Feb 2014
Qscan=[0.168 – 0.28]
Qspeed: 1.24e-5/sec (rate at which exc. Tune is changed)
WP=(0.1486, 0.3726) ; Qs=0.0056
0.2151
0.2103
0.2329
1e-3
2.2e-3
6e-4
So, we are a bit lost about the reason for these peaks.
Suggestions are welcome
Nevertheless, let’s try to see if we can see some lifetime drop between this forest of peaks

## Slide 10
Moving frf by -2kHz ;
E=2.994GeV
Nominal RF frequency ;
E=2.984GeV
Two tests at different frf
There seems to be a valley in the lifetime product, which moves consistently with the frf.
But it is very difficult to distinguish it among the peaks, where the lifetime increases

## Slide 11
Looking at DCCT and BLD
DCCT Lifetime
BLD counts
Rather than a sudden drop, we are looking a slow decay

## Slide 12
Energy Determination
Raw Data
BLD Evolution removing data when sy>1.10*sy
0.2289
0.2352
0.2224
According to these peaks in BLD, energy is 2.9837+/-5e4 GeV
(only presentable in a DEELS workshop)
Data manipulation based on the beam size evolution

## Slide 13
Summary and Questions
The energy scans at ALBA have been limited by the presence of non understandable resonances
These resonances produce vertical beam size increase, which make the lifetime to increase
To detect the resonances, best monitor is the beam size
To detect losses, best monitor is the scintillator based BLD
All in all, the drops in lifetime or sudden increases in BLD seems to indicate a beam energy of 2.984 GeV
Precision cannot be fully determined due to the presence of these peaks.