## Slide 1
Maher Attal
On behalf of
SESAME Team
Status of SESAME
Synchrotorn-light for Experimental Science and Applications in the Middle East
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014
Allan, Jordan

## Slide 2
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014
Introduction
 SESAME is an interregional 3rd generation light source being constructed in Jordan
(in Allan, 30km west of Amman) and expected to serve the user community in the Middle
East region.
 SESAME machine composes:
 BESSY I injector (22 MeV classical Microtron + 800 MeV Booster)
 completely new 2.5 GeV storage ring.
 mixture of donated ( by SLS, HZDR, LURE, Daresbury) and new beamlines.

## Slide 3
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014
Microtron + TL1 Commissioning
 Full energy beam at Microtron exit (~22MeV) Nov. 28, 2011.
 Full energy beam at end of Microtron-Booster transfer line
(~22MeV) March 27, 2012.
SESAME Microtron Main Parameters
Extractable energy 5.3-22.5MeV
Extractable turns 10 – 42
Energy gain / turn 535 keV
Energy spread(FWHM) 35keV
Magnetic field 0.112T
Microwave frequency, power 3GHz, 2MW
Pulse duration 2s
Beam power 400kW at 21MeV
H-emittance 3.8 m.rad (100% of the beam @ 21MeV)
V-emittance 12.8 µm.rad (100% of the beam @ 21MeV)
3 mm
4.4 mm

## Slide 4
Booster Commissioning Results
Booster
Transfer
line TL2
TL1
Microtron
Main Booster parameters
Injection energy 20MeV
Extraction energy 800MeV
Circumference 38.4m
H-emittance 300 nm.rad
V-emittance 30 nm.rad
Mom. com. factor 0.18
RF frequency 500MHz
RF max. power 2kW
Operation freq. 1Hz
Inj. kicker pulse ~ 4.5µs
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014

## Slide 5
 The first turn beam (July 15, 2014).
 No correctors are used.
 Few turn beam (July 16, 2014).
 No correctors are used.
 using model values (QF= 2.83A, QD= -2.18A, Dipole= 24.96A)
 Varying injection angle.
 optimizing amplitude and timing of injection kicker kick.
 Multi turn beam (thousands) (July 17, 2014).
 Varying magnets current slightly from model values.
 Modifying slightly injection angle.
 0.2A in Corr. 3 enhanced the transmission substantially.
Booster Commissioning Results
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014

## Slide 6
Characterizing the DC Mode
 RF paramaters
 Varying RF phase had no noticeable effect on the beam current in the Booster.
 The theoretical RF frequency 499.654MHz showed almost the best performance.
 Tune measurement
 Horizontal tune was measured easily using the beam injection oscillations.
 Vertical tune was measured by injecting the beam with vertical angle (shaker is not
ready yet).
 Three working points have been found as a result of scanning:
1- (2.22, 1.31), a working point mentioned in BESSY documents.
2- (2.22, 1.40)
3- (2.28, 1.47)
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014

## Slide 7
1- The point (2.22, 1.31) obtained for (QF = 2.67A, QD = 2.14A)
(corresponding model values are QF = 2.83A, QD = 2.18A).
It has low beam current transmission & low beam lifetime as shown by DCCT.
DCCT signal
2- The point (2.22, 1.4) obtained for (QF = 2.68A, QD = 2.27A).
It realizes better transmission with beam lifetime ~ 100ms.
Characterizing the DC Mode
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014

## Slide 8
Characterizing the DC Mode
3- The point (2.28, 1.47) for (QF = 2.77A, QD = 2.47A).
It realizes good transmission with the best beam lifetime ~ 150ms.
Theoretical beam lifetime @20MeV is ~ 150ms if the Booster average pressure is 5e-7 mbar.
 Betatron function measurement
 Measure Qx versus kQF and kQD.
 use the formula , N: number of family quadrupoles, Lq = 0.256m.
< x > = 4.65m @ QF (theoretical value is 5.3m) .
< x > = 0.94m @ QD (theoretical value is 1.12m) .
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014

## Slide 9
Characterizing the DC Mode
 Dispersion function measurement
 Measure orbit position x for RF frequency fRF.
BPM1 showed x = 2.3 mm for fRF = -100 kHz.
 using the formula , and theoretical c = 0.18.
x = 2.06m (theoretical dispersion = 1.6m)
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014
The fluctuating beam was always a prominent source of measurement error.

## Slide 10
Energy Ramping Mode
 Beam energy was ramped successfully to 800MeV
(Sep. 17, 2014).
 Ibeam = 1.3 mA (~ 1.7% injection efficiency)
 Injection was done at 23.9 ms delay in a semi-flat top
region in the dipole current ramping curve.
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014
Chart: Dipole current ramp
Chart: 
Injection moment
RF voltage
Dipole current
 The ramping curve started with the working point (2.22, 1.4) .

## Slide 11
Energy Ramping Mode
 Ibeam = 4 mA (~ 5% injection efficiency) was achieved
(Oct. 29, 2014).
 Another dipole current curve was used without
a flat-top region (injection on the fly).
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014
Injection moment
Chart: Dipole current
 The RF voltage ramping curve started with 5kV
and ended with 70 kV (injection voltage = 8kV).
RF voltage ramping curve
* Beam fluctuation due to instability
in electrostatic injection septum.

## Slide 12
Beam Images at Different Energies
 The electron beam was imaged at different energies (during the ramping)
using the added Visible Light Diagnostic beam line.
 The beam size was roughly measured over the ramping time.
100ms (~120MeV) 300ms (~440MeV) 500ms (~735MeV) 640ms (~800MeV)
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014
Chart: ramp time [ms]
| 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550
 | 1.2 | 0.8 | 0.6 | 0.55 | 0.55 | 0.6 | 0.8 | 0.9 | 1
 | 1.2274 | 1.0685 | 0.79073 | 0.7092 | 0.71879 | 0.75324 | 0.79144 | 0.83547 | 0.86113
Chart: ramp time [ms]
| 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550
 | 1.6 | 1.2 | 0.9 | 0.6 | 0.4 | 0.2 | 0.2 | 0.2 | 0.2
 | 1.6993 | 1.3617 | 1.1004 | 0.81906 | 0.5526 | 0.32959 | 0.21199 | 0.19009 | 0.19272

## Slide 13
Booster Commissioning was done under Hard Conditions
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014
13
December – April, 2014
November, 2014
 The new roof
is expected to
be ready by
Feb. 2015.
Tune measurement during ramping
 Although no impact was seen on the acceleration
efficiency, nevertheless the tune drift can be easily
corrected.

## Slide 14
Storage Ring Characteristics
 Main 2.5 GeV Ring parameters:
 Simple DBA lattice (2 quadrupole families, 2 sextupole families) with dispersive sections.
 C = 133.2 m, Emitt. = 26 nm.rad.
 (Qx , Qy ) = (7.23, 6.19).
 Bending magnet: B0 = 1.455T, g = -2.79T/m.
 16 straight sections (8x 4.4m + 8x 2.4m).
 Up to 25 beamlines ( 13 from dipoles + 12 from insertion devices).
x
y
x
Super-period.
The ring is composed
of 8 super-periods.
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014

## Slide 15
Storage Ring Status: Magnets
 Storage ring magnets are constructed through CESSAMag project in the frame of
SESAME-CERN/EU collaboration.
 Dipole (constructed by TESLA, UK) prototype is being magnetically
measured at ALBA.
All dipoles to be delivered by Sep. 2015.
 Quadrupole prototype is being assembled
(by Elytt-Spain, coils by STS-Turkey).
First batch to be measured at CERN by
March 2015.
 Sextupole prototype (by CNE-Cyprus & HMC-3-Pakistan, coils by
SEF-France) has been magnetically measured at CERN.
First batch to be measured at CERN by March 2015.
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014

## Slide 16
Storage Ring Status: RF System
 The 500MHz RF system is composed of 4 RF plants.
Each plant composes:
- 120kW Elettra cavity (detuned up to ±2MHz).
 Collaboration agreement was signed with Elettra.
 Delivery of 4 cavities foreseen by May 2016.
- 80kW solid state amplifier(the 1st to be built by SOLEIL,
the 3 others by Sigmaphi-SE).
 Construction to start soon.
- WR1800 waveguide (inkind contribution from DESY)
- Digital LLRF (in the tendering process)
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014
Courtesy
of SOLEIL

## Slide 17
Storage Ring Status: Vacuum Chamber
 The ring contains 16 valves, 64 bellows, 32 BPMs + 32 ID BPMs.
 Contract has been signed with FMB.
 Expected delivery date of prototype is Feb. 2015.
 To be setup with magnets and prototype girder at CERN by March 2015.
 Valves, bellows, pumps
injection section, RF
section to be contracted.
One cell vacuum chamber
BPM
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014

## Slide 18
Storage Ring Status: Girders
 Flatness < ± 50 µm, Pin-positioning < ± 50 µm, Deflection under load < 50 µm.
 Contract has been signed with Nortemecanica, Spain.
 Prototype delivery expected by Feb. 2015. To be setup with magnets & vacuum chamber
at CERN by March 2015 (SAT).
 Last batch to SESAME by May 2016.
5.2m
0.9m
0.953m
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014

## Slide 19
SESAME Phase 1- Day 1 Beam Lines
No. | Beamline | Energy | Photon Source | Comment
1 | Protein Crystallography | 4 – 14 keV | IV Undulator ? | Under discussion
2 | XAFS / XRF (BASEMA) | 4.5 – 30 keV | Bending Magnet | Helmholtz-Zentrum Dresden-Rossendorf/ESRF. New focusing components. New hutch
3 | IR Spectromicroscopy (EMIRA) | 0.01 – 1 eV | Bending Magnet | Completely new beam line
4 | Powder Diffraction | 5 – 25 keV | 2.1T Wiggler | SLS (with source)
5 | Soft X-ray, Vacuum Ultraviolet (VUV) | 0.05 – 2 keV | Ellipt. Polarizing Undulator | Completely new beam line
6 | SAXS / WAXS | 8 – 12 keV | Bending Magnet | Daresbury
7 | Extreme Ultraviolet (EUV) Spectroscopy | 10 – 200 eV | Bending Magnet | Daresbury & LURE
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014

## Slide 20
 (BASEMA) XAFS/ XRF beam line:
 CDR approved.
 Manual user documentation finished.
 Installation to be started in 2015.
 (EMIRA) IR beam line:
 Collected from main and edge dipole field.
 Tendering process is being processed.
 Expected to be functional by mid 2016.
SESAME Phase 1- Day 1 Beam Lines
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014
Dipole chamber
Protection wall
Diamond window
Experimental station
Branch 1
Branch 2

## Slide 21
Storage Ring Milestone Schedule
Deliverables | Contracted | Prototype | 1. Batch | Last Batch
Magnets (Dipole) | 08.2013 | 10.2014 | 02.2015 | 10.2015
Power-supplies | 05.2014 | 10.2014 |  | 06.2015
Vacuum Chamber | 01.2014 | 02.2015 | 05.2015 | 10.2015
Girder | 08.2014 | 02.2015 | 09.2015 | 05.2016
Cavities | 05.2014 |  | 12.2015 | 05.2016
RF-Amplifier | 10 -11.2014 (SOLEIL - Sigmaphi) |  | 11.2015 (SOLEIL & Sigmaphi) | 08.2016 (Sigmaphi)
 Storage ring commissioning expected by 1st of 2017.
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014

## Slide 22
Thank you
M. Attal, XXII ESLS Workshop, ESRF, Nov. 25-26, 2014