## Slide 1
Femto-Slicing project at SOLEIL
M.-A. Tordeux
on behalf of the Femto-Slicing project team

## Slide 2
Outline
Motivation for a Femto-Slicing project
SOLEIL specificities
Setup
Commissioning
Outlook

## Slide 3
cor
SDC6
SDM8
SDM7
SDC7
SDM6
1) One single laser Ti:Sa 800 nm, 5 W, 1 kHz, 30 fs-fwhm for the machine and for the CRISTAL beamline
dipole
SOLEIL specificities
Laser
Beam

## Slide 4
cor
Modulator
Wiggler
SDC6
SDM8
Laser
Beam
SDM7
SDC7
SDM6
2) Modulator = a wiggler used for femto-slicing and as a source for PUMA beamline
Wiggler Type | Hybrid out-vacuum
Magnetic period | 164.4 mm
Period number | 20
Magnetic gap | 14.5 mm – 240 mm
Magnetic components | Poles: VACOFLUX50 (Saturat. field: 2.35 T) Magnets: VACODYM 764 TP (magn.: 1.37 T)
Max. magnetic field | 1.81 T
SOLEIL specificities
PUMA BL

## Slide 5
cor
SDC6
SDM8
Laser
Beam
SDM7
SDC7
SDM6
Core
3 mm
Slice
Effective Dispersion
Deff (m)
S (m)
3) Slice separation using
the machine’s horizontal dispersion function
Modulator
Wiggler
Additional chicane to reduce the photon emission angle
SOLEIL specificities
Shifted diaphragm in BL frontend

## Slide 6
cor
Laser
Beam
CRISTAL
(U20)
TEMPO
(HU44 + HU80)
DEIMOS
(HU52 + HU65)
GALAXIES
(U20)
Modulator
Wiggler
4) Delivery to several beamlines:
2  Phase 1  beamlines (CRISTAL, TEMPO)
2 beamlines under study (DEIMOS, GALAXIES)
1 extra possible beamline ? (SEXTANTS)
75 fs
SOLEIL specificities
80 fs
140 fs
210 fs
300 fs
75 fs

## Slide 7
Setup
Laser: 80 m transport line from CRISTAL Laser hutch to interaction point under primary vacuum
0 : Wiggler
DIAG_IR
DIAG_101
DIAG_01
DIAG_103
ENC104
ENC105
DIAG_20
DIAG_02
ENC103
ENC102
ENC101
LASER
Output
MgF2
DIAG_00
55 m
LASER ROOM
LENS 9 m
PUMA BL
MgF2
STORAGE RING ROOF
STORAGE RING TUNNEL
CRISTAL BL
EXPERIMENTAL HALL
DIAG_001
Wiggler
5 mirrors under x-y remote control
5 centering diagnostics
1 pointing diagnostic
Foreseen position feedback

## Slide 8
Setup
Infra-Red Diagnostics: measure the overlaps between Laser and SR radiations
 inside the Storage Ring tunnel,
under the PUMA beamline frontend.
0 : Wiggler
DIAG_IR
MIR 001
WIN 001
FGL 610
LEN 100
MIR 002
Spatial overlap:
Optics + CCD for imaging in the wiggler
Basler
Spectral overlap:
    Spectrometer
    Ocean Optics USB2000
    Temporal overlap:
    Fast photodiode
    FPD 310-FV from Menlo
Wiggler
In Vacuum Cu Mirror
Saphhire Window
Filters
2.5 m Lens
Rmax Mirror
900 mm
300 mm
STORAGE RING TUNNEL
Translation stage for CCD
Optical fiber

## Slide 9
Setup
fs pulses  CRISTAL BeamLine
Wiggler
Laser
PUMA BeamLine
THz pulses extracted @ AILES beamline
fs pulses 
TEMPO BeamLine
THz Diagnostics: evaluates the dip in the beam core using the THz beamline AILES
    High sensitivity measurements:
    Bolometer
    QMC 1 ms, SAI card
    IR Labs 1.7 µs, oscillo Lecroy 1GHz
Fast measurements (turn by turn):
    THz diode
    Virginia Diode Virginia 1 nsdiodes)
10 m
-1 0 1
Time (ps)
1
0
-1 0 1
Time (ps)
1
0
laser

## Slide 10
Commissioning
Difficult issues
Transport of laser:
Two steps of alignment: use of a focused mode for first alignment with electrons (minimizes diffraction / reflections in narrow chambers), then use of the collimated mode.
IR Diagnostics:
  Inside the Storage Ring tunnel  lack of access !
  Strong difference in intensity between laser and SR
  Imaging system suffering from distortion at Ie- > 1 mA.
  still under investigation
1 2 3 4 mA
1
2
wiggler
wiggler

## Slide 11
Commissioning
Chronology
Start of commissioning: late Dec 2013
Dedicated time during shutdowns for some laser mirror re-alignment, laser diagnostic optimization.
20 dedicated machine sessions (often too short..) for :
  Alignment of IR diagnostics on the Synch. Radiation and setup optimization
  Alignment of laser up to IR diagnostics board
  Optimization of the whole protocol for interaction
  Three 12h sessions for systematic interaction test (e- bumps, synchronisation)
  On the 3rd one (September 29), we changed bolometer, from the 1 ms to the 1.7 µs response time one. Interaction is seen..

## Slide 12
Commissioning
(1) Alignment in the Wiggler of SR and laser (in focused mode and low power)
Wiggler entry
1 pixel on the CCD ≡ 20 µm in the transverse plane of the wiggler
Wiggler middle
Wiggler exit
SR
Laser

## Slide 13
Commissioning
(2) Change of the laser mode (collimated, 4 W)
No straight forward measurement of the spectral overlap (presence of filters on the IR diagnostics board)
  Measure the laser spectrum in the laser hutch
  Define the central wavelength
  Adjust the wiggler gap to the resonant wavelength
Wiggler gap [mm] | Lambda Res [nm] from magnetic measurements
14.5 | 941.7
15 | 902.07
15.5 | 864.61
16 | 829.86
16.3 | 810.01
16.4 | 803.60
16.5 | 797.17
16.6 | 790.9
16.7 | 784.68
16.8 | 778.51
17 | 766.53
20 | 618.73
(3) Adjustment of the spectral overlap
Laser

## Slide 14
Commissioning
(4) Synchronisation
  Measure arrival time of the SR on the photodiode, without laser.
  Add filters, open the laser shutter, adapt the optical fiber to equal SR and laser intensity level.
  Measure arrival time of the laser, adjust the laser delay to equal the SR’s.
  Final resolution: 10 ps
SR
Laser
1 ns

## Slide 15
Commissioning
1st turn
2nd turn
3rd turn
4th turn
  After a rough optimisation, we saw signals for up to 4 turns with the fast diode (0.3 – 0.5 THz BW).
First results : THz intensity measurement
1 kHz trigger
Bolometer signal = Interaction !!
  With the bolometer (0.1 – 3 THz BW), we saw signals of a few V at laser repetition rate.

## Slide 16
Commissioning
Very first optimizations versus THz signal
e- vertical bump (µm)
U bolometer (V)
e- horizontal bump (µm)
U bolometer (V)
U bolometer (V)
U bolometer (V)
Laser focusing (afocal in mm)
Laser delay (ps)

## Slide 17
2015
2014
2016
2017
CRISTAL
fs-TR EXPERIMENT @ 1 kHz
INSTRUMENT
BASIS OK
BT Implementation
fs-Xph on CRISTAL
Detect - Optimisation
THz
Optimisation
1 kHz – 5 W LASER SYSTEM Management
5 kHz LASER SYSTEM
OTCX Implementation
BT Implementation
CRISTAL
fs-TR EXP. @ 5 kHz
XPh Detect/Optim
on CRISTAL
THz
Optimisation
THz
Caract.
BT
OK
5 kHz – 25 W LASER SYSTEM Management
TEMPO
fs-TR EXPERIMENT @ 1 kHz
Chicane impl.
Outlook
DEIMOS, GALAXIES, SEXTANTS slicing feasibility study
BT = Laser Beam Transport

## Slide 18
Sources and Accelerators Division
Head of the project (Accelerator part): A. Nadji
Deputy : M.-E. Couprie
Commissioning coordinators: M. Labat and M.-A. Tordeux
Accelerator physics: M.-A. Tordeux, P. Brunelle, L. S. Nadolski, A. Loulergue
Diagnostics: M. Labat, L. Cassinari, F. Dohou, D. Pedeau, J.-P. Ricaud
Insertion Devices & Chicane: O. Marcouillé, T. El Ajjouri,
H. Abualrobf, F. Marteau, J. Vétéran, M.-E. Couprie.
Steering committee: M.-E. Couprie, J. Luning, P. Morin, A. Nadji, P. Prigent
Technical Division
Vacuum: C. Herbeaux, N. Béchu
Mechanical Engineering: J.-L. Marlats, D. Zerbib, S. Génix, K. Tavakoli, A. Mary
C. De Oliveira, C. Créoff , S. Bonnin
Survey and Alignement: A. Lestrade, M. Ros
Infrastructure: P. Eymard, P. Goy
General Division
Radiation safety: J.-B. Pruvost, M. Hafsi, F. Ribaud
Laser Safety: L. Germain, J.P. Laurent
Methods: H. Rozelot
Experiences Division
Head of the project (Experience part): J. Luning
Deputy: P. Prigent
Commissioning coordinators: P. Hollander, CRISTAL, TEMPO
Instrumentation & Coordination: P. Hollander, P. Prigent
Detectors : S. Hustache
Optics: F. Polack, T. Moreno
CRISTAL Beamline: C. Laulhé, S. Ravy
TEMPO Beamline: M. Silly, F. Sirotti
Computer Division
(ECA) S. Zhang, J. Bisou, Y.M. Abiven
(ISI) E. Moge, P. Gattoni
(ISG) J. Guyot
(ICA) O. Roux, S. Le
Femto-slicing project team