## Slide 1
Stretched wire measurement R&D at the ESRF SW impedance and SW tomography
Gaël Le Bec
21st International Magnetic Measurement workshop
Grenoble, 24-28 June 2019

## Slide 2: Outline
Stretched wire impedance measurement
Stretched wire tomography
Conclusion

## Slide 3: Outline
Stretched wire impedance measurement
Stretched wire tomography
Conclusion

## Slide 4: Streched wire impedance Measurement
Principle
Coil
Induced voltage
Magnetic flux
Time-varying fields and/or coil motion
Fluxmeters
Search coils
Rotating coils
Moving stretched wire
Time-varying flux

## Slide 5: Streched wire impedance Measurement
Principle
Coil
Time-varying flux
Static field
Induced voltage
Magnetic flux
Coil motion
Local meas.
Accurate displacement of a coil?
(e.g. installed on an undulator bench)
Needs side access
Integrators, etc…
Current driven coil deformation?
Use a vibrating wire!

## Slide 6: Streched wire impedance Measurement
Principle
I
Mechanical deformation of the wire
Vibrating and pulsed wire methods

## Slide 7: Streched wire impedance Measurement
Principle
I
Current and voltage measurements
Stretched wire impedance method

## Slide 8: Streched wire impedance Measurement
Principle
Faraday’s law
Area cut by the wire motion
Induced voltage
The wire as an inductive behavior
Its impedance varies with
Impedances measured at different wire modes may give information on the field variations along the wire
Can we measure this effect? Is it completely negligeable?

## Slide 9: Streched wire impedance Measurement
Equations of the wire impedance
Field along the wire:
(considering only one field component, neglecting transverse field variations, neglecting dispersion)
Wire’s transverse position:
with
and
(see [Temnykh, NIMA, 1997] for the vibrating wire equations, [Le Bec, IMMW19, 2015] for the terms)
wire length
wire tension
linear mass density
damping coef. x linear mass dens.

## Slide 10: Streched wire impedance Measurement
Equations of the wire impedance
Induced voltage
=I
Inductance of the wire
Depends on + integrals of oscillation terms

## Slide 11: Streched wire impedance Measurement
First tests
A (PM) quadrupole was installed on a stretched wire measurement bench
A 0.1 mm diameter Al99Si1 wire was used
Impedance spectrum
Significant signal for the first harmonics
Weak signal for the higher harmonics
 the magnet is not centered longitudinally
DC
13.2 Ω
h1
250 Ω
h2
16.3 Ω
h3
20.7 Ω
h5
13.6 Ω

## Slide 12: Streched wire impedance Measurement
First tests
A (PM) quadrupole was installed on a stretched wire measurement bench
A 0.1 mm diameter Al99Si1 wire was used
Impedance at first harmonic
Compared to standard SW measurements (squared)
dependence observed

## Slide 13: Streched wire impedance Measurement
Possible applications
Field measurements?
May be used to measure average field (h1) and gradient (h2)
Low longitudinal resolution expected (weak signal for higher harmonics)
Scale factor to be investigated in more details
Polarizarion needed for weak field measurements
Provide additional information during moving or vibrating wire meas.
Very simple setup
May be used to lock-in the first wire modes
Sensitive to the longitudinal centering of the magnet (h2)

## Slide 14: Outline
Stretched wire impedance measurement
Stretched wire tomography
Conclusion

## Slide 15: Stretched wire tomography
Tomographic reconstruction
Widely used in medical CT-scans
Widely used in synchrotron light sources facilities
Signal
X-ray detecor
X-ray source
angles
position
position
angle
Acquisition
Radon transform
Reconstruction

## Slide 16: Stretched wire tomography
Tomographic reconstruction
X-ray tomographs measure the Radon transform of an object

## Slide 17: Stretched wire tomography
Tomographic reconstruction
X-ray tomographs measure the Radon transform of an object
Projection, i.e. integrals

## Slide 18: Stretched wire tomography
Tomographic reconstruction
X-ray tomographs measure the Radon transform of an object

## Slide 19: Stretched wire tomography
Tomographic reconstruction
X-ray tomographs measure the Radon transform of an object

## Slide 20: Stretched wire tomography
Tomographic reconstruction
X-ray tomographs measure the Radon transform of an object
Definition of the Radon transform
straight line

## Slide 21: Stretched wire tomography
Tomographic reconstruction
X-ray tomographs measure the Radon transform of an object
Reconstruction methods
Ill-posed problem
Filtered Backprojection (standard function in Matlab, Mathematica, etc.)
Iterative methods
…
Stretched wire induced voltage:
This is a projection of the field! Local values of the field can be computed from a set of SW measurements.
But what is the link with stretched wire magnetic measurements?

## Slide 22: Stretched wire tomography
Simulation of a SW tomography experiment
Modelization of a PM block with the Radia code
Assumption: easy-axis distribution dominated by the field applied during die pressing  easy-axes follows field lines  A 2nd order model of the applied field was used (16 parameters)
View of the 3D model of the PM block.
M
Direct field computation (Radia)
Set of field integrals, i.e. Radon transform
Inverse Radon transform (filtered backprojection)

## Slide 23: Stretched wire tomography
Simulation of a SW tomography experiment
Reconstruction of a 2D field map
Needs a lot of angles for reconstruction
 Long acquisition time!
Identification of model parameters
Reduced number of angles
Magnet dimensions known
Easy-axis distribution in the PM block
View of the 3D model of the PM block.
M
Direct field computation (Radia)
SW measurements at 3 angles
Reconstruction from parameters (easy-axis) identification

## Slide 24: Stretched wire tomography
First tests
Acquisition sequence
Go to initial position
Rotate the stage to
Translate and acquire the voltage
Rotate the stage to
…
Main parameters
samples
±100 mm translation
Sample to wire: 4 mm
Hardware
Newport stages and drivers
Keithley K2182 voltmeter
M
Stretched wire
Rotating stage
Linear stage
Experimental setup
PM sample

## Slide 25: Stretched wire tomography
First tests
Measured field integrals
Angles
Positions
Magnetic field map (filtered backprojection)
M
Stretched wire
Rotating stage
Linear stage
Experimental setup
PM sample

## Slide 26: Stretched wire tomography
To do
Extract the position and orientation of the sample
Try the parameter identification based reconstruction on real samples
Refine the magnetization distribution model
Design a dedicated bench
…
M
Stretched wire
Rotating stage
Linear stage
Experimental setup
PM sample

## Slide 27: Stretched wire tomography
To do
Extract the position and orientation of the sample
Try the parameter identification based reconstruction on real samples
Refine the magnetization distribution model
Design a dedicated bench
…
M
Stretched wire
Rotating stage
Linear stage
Experimental setup
PM sample

## Slide 28: Outline
Stretched wire impedance measurement
Stretched wire tomography
Conclusion

## Slide 29: Conclusion
Two measurement methods developed
Stretched wire impedance
The wire impedance varies with
Demonstrated experimentally
Low longitudinal resolution, but almost for free
Stretched wire tomography
SW meas are projections
Radon transforms of the field can be measured
Demonstrated experimentally
May give information on magnetization distribution
Data processing to be further developped

## Slide 30: Acknowledgments
Insertion devices and magnet group
Christophe Penel
Marceau Neufselle
Joel Chavanne

## Slide 31: Many thanks for your attention