## Slide 2: SAFETY RULES FOR THE ANALYSIS OF BIOLOGICAL SAMPLES AT THE ESRF AND OVERVIEW OF THE LABS ON SITE
26/07/2013
Page <number>
Presentation User meeting/VM-2019
Regulation applied (European and French)
Microorganisms and GMO
Structural Biology samples
Human samples and or derivatives
Live animals
- ESRF-ILL Joint proposals
*Safety requirements and measures
*Constrains and lab facilities access
*Waste management
http://www.esrf.fr/Infrastructure/Safety/Experiments/Biology_Experiments

## Slide 3: SAFETY RULES FOR THE ANALYSIS OF BIOLOGICAL SAMPLES AT THE ESRF AND OVERVIEW OF THE LABS ON SITE
26/07/2013
Page <number>
Presentation User meeting/VM-2019
Microorganisms
Only class 1 and 2 risk microorganisms (3 and 4 strictly forbidden)
Live or Dead microorganisms
  If live organisms
    Access to proper lab for microorganism culture if any (difficult, only EMBL lab support and only class 1 risk).
  If GMO clones brought on site, license number and date of release (origin country)
  If GMO clones stored on site, a “DUO” application is submitted by ESRF safety
  Risk analysis required (detailed) and lab access requested
  No controlled agent authorized anymore.
If fixed (dead) microorganism
  Loses its class of risk hence no biological risk, no constrain
    Shipped by authorized carrier highly recommended.
http://www.esrf.fr/Infrastructure/Safety/Experiments/Biology_Experiments/use-of-micro-organisms-or-derivatives

## Slide 4: SAFETY RULES FOR THE ANALYSIS OF BIOLOGICAL SAMPLES AT THE ESRF AND OVERVIEW OF THE LABS ON SITE
26/07/2013
Page <number>
Presentation User meeting/VM-2019
Structural biology samples
http://www.esrf.fr/Infrastructure/Safety/Experiments/Biology_Experiments/macromolecular-samples

## Slide 5: SAFETY RULES FOR THE ANALYSIS OF BIOLOGICAL SAMPLES AT THE ESRF AND OVERVIEW OF THE LABS ON SITE
26/07/2013
Page <number>
Presentation User meeting/VM-2019
Two regulations, one for imported samples and one for samples already on French territory (IE number – DC number)
Applies to Dead fixed tissues or cells or Fresh tissues and cell lines
    Human samples authorization for importation - exportation
      ESRF authorization renewed every 5 years; 2017; next 2022
      Every user samples is added as an annex to ESRF “master” authorization
      Dossier set-up and review by authorities accounting two months
      DC (« déclaration de conservation ») number
      Every French structure storing human samples even cell lines commercially supplied
Human samples and/or derivatives (in theory)
http://www.esrf.fr/Infrastructure/Safety/Experiments/Biology_Experiments/samples-from-humans-and-or-derivatives

## Slide 6: SAFETY RULES FOR THE ANALYSIS OF BIOLOGICAL SAMPLES AT THE ESRF AND OVERVIEW OF THE LABS ON SITE
Dead fixed tissues or cells
        - No biological risk once chemically fixed (formaldehyde but caution for PrPSc)
Fresh tissues or cells
      - Innocuousness for being on beam lines and samples contained if class 2 risk. UV inactivation on specific beam lines
  - Access to CL2 lab in case of cell culture needed (training required) hence, Cell risk analysis document mandatory and BMF form.
      - Fresh tissues must be both risk-free and contained AND especially in vacuum chambers, test for Prions mandatory, otherwise should be in hermetic sealed container.
      - If not, refused.
  Detailed Risk analysis required, minimum 2 weeks in advance
    No waste managed on ESRF site for human samples and or derivatives : samples returned back to home institute
26/07/2013
Page <number>
Presentation User meeting/VM-2019
Human samples and/or derivatives, (in practice)

## Slide 7: SAFETY RULES FOR THE ANALYSIS OF BIOLOGICAL SAMPLES AT THE ESRF AND OVERVIEW OF THE LABS ON SITE
26/07/2013
Page <number>
Presentation User meeting/VM-2019
Animal samples
Dead animals
  VET certificate (fresh or fixed tissues)
  CITES (for protected or endangered species)
    Set-up to comply with beam line environment (vacuum chambers)
      Samples brought by Users or shipped through store by authorized carrier
Live animals
  AP (“project authorization”) required after ETHAX validation and French authorities registration (5 years validity)
    Animals purchased by ESRF (BMF form updated) or brought by Users (specific cases)
    Users certified (national certification, e.g. PIL / PPL) or equivalent for handling animals (otherwise support mandatory from BMF)
    Detailed Risk analysis required at least 2 weeks in advance
    Drugs details and purchased by ESRF, no drugs brought by Users

## Slide 8: SAFETY RULES FOR THE ANALYSIS OF BIOLOGICAL SAMPLES AT THE ESRF AND OVERVIEW OF THE LABS ON SITE
26/07/2013
Page <number>
Presentation User meeting/VM-2019
ILL-ESRF JOINT proposals
Samples used on both instruments Sample sheets mandatory on both site
    If ESRF first: no problem, except if D2O or Deuterium used
    registration of D2O and deuterium required in advance
    Radiation-Protection (RP) authorization required
    max 1kg/year only in total at the ESRF reduced volume or deuterium quantity
    D2O waste taken back by Users
  If ILL first: potential risk of activation  control by both ILL AND ESRF RP services with at least 1 day lap between the ILL and ESRF sessions.
    Samples to be cleared by ILL RP with certificate and then stored in the
    « RP lab » at ILL.
    ESRF RP will come and check samples on ILL site.
    Samples authorized on ESRF site only once cleared ESRF RP.
    Notification and Appointment with ESRF RP to be scheduled in advance.

## Slide 9: SAFETY RULES FOR THE ANALYSIS OF BIOLOGICAL SAMPLES AT THE ESRF AND OVERVIEW OF THE LABS ON SITE
Laboratories available on site for biological samples :
- EMBL lab support (SAXS, Microorganisms, etc)
To be requested at least 4 weeks in advance using the form available on the website or via A-form as soon as equipment are not available on ESRF site. Only two people per User group allowed in facilities and specific training first by EMBL safety officer. Please register with : lab_support@embl.fr
- BMF labs (L1, L2, Histology lab, Sample lab, etc)
To be requested at least 6 weeks in advance for managing animals, consumables, drugs and labs bookings. Specific training for access to CL2 lab. Please register with : bmf@esrf.fr and expsaf@esrf.fr
- Other labs (Cryo-EM, CryoBench, Science Building, etc)
To be requested in advance for booking and consumables
In labs, same rules and regulation apply as for beam lines.
Local contact responsible for organizing contacts with lab responsible people.
Waste management specific for each institute.
26/07/2013
Page <number>
Presentation User meeting/VM-2019

## Slide 10: SAFETY RULES FOR THE ANALYSIS OF BIOLOGICAL SAMPLES AT THE ESRF AND OVERVIEW OF THE LABS ON SITE
26/07/2013
Page <number>
Presentation User meeting/VM-2019
https://www.esrf.eu/UsersAndScience/UserGuide/Preparing
Biological experiments ESRF
http://www.esrf.fr/Infrastructure/Safety/Experiments/Biology_Experiments
Support Laboratories Request Forms
http://www.esrf.fr/UsersAndScience/UserGuide/Preparing/laboratories
Shipping Samples
https://www.esrf.eu/UsersAndScience/UserGuide/Preparing/ImportingEquipment
Safety information for users
https://www.esrf.eu/UsersAndScience/UserGuide/safety-information
Where to find more information

## Slide 11: SAFETY RULES FOR THE ANALYSIS OF BIOLOGICAL SAMPLES AT THE ESRF AND OVERVIEW OF THE LABS ON SITE
THANK YOU
26/07/2013
Page <number>
Presentation User meeting/VM-2019