## Slide 1: Emittance exchange in electron booster synchrotron by coupling resonance crossing
Jonas Kallestrup :: Paul Scherrer Institute
European Synchrotron Light Source workshop 2020

## Slide 2: Why emittance exchange?
SLS 2.0 plans for injection procedure in three stages:
  Horizontal off-axis injection with kicker-bump
  Aperture-sharing with short-pulse kicker (10 ns pulse length)
  Longitudinal on-axis injection with ultra short-pulse ( 2 ns)
Dynamic aperture needed for horizontal kicker-bump injection:
Booster synchrotrons:
Decrease by exchanging
Several benefits:
  relaxed requirement
  relaxed septum blade thickness
  relaxed bump amplitude

## Slide 3: Ways to emittance exchange
Arrangement of skew quadrupoles in transfer line
  requires 5 skew quads + dispersion-free transfer line
Linear difference resonance crossing in booster synchrotron
  no additional magnets needed
  requires good flexibility to modify booster-ramps
Pulsed- or AC-skew quadrupole

## Slide 4: Why emittance exchange by coupling resonance crossing?
Emittance exchange by crossing linear difference resonance:
  Only small tune changes required  No change to the linear optics
Things to consider:
Damping
  Do exchange shortly before extraction
Transverse coupling
  Small coupling requires slow crossing
    i.e. more damping
For details, see:

## Slide 5: Measurements in SLS booster
Highlights
First booster built specifically for top-up operation
Mounted on inner wall of Storage Ring tunnel
  ≈ same circumference as SR
Low horizontal emittance: nm
  Vertical emittance ~2-3 nm (theoretical minimum of 0.05 nm)
Digital magnet power supply control
  Flexible and easily controllable!

## Slide 6: Measurements in SLS booster
Implementation at the end of ramp
Extraction
Injection
Extraction
Injection

## Slide 7: Measurements in SLS booster
Beam sizes measured in transfer line
Factor ≈4 decrease in
  Limited by vertical emittance (≈2-3 nmrad)
(different optics for visualization)

## Slide 8: Measurements in SLS booster
Improvement of and (see SLS status talk from yesterday)
  Factor decrease in
  Very valuable improvement for SLS 2.0!

## Slide 9: Non-adiabatic crossing
Mismatch between |C| and crossing speed  “Non-adiabatic exchange”
Simulation
Experiment

## Slide 10: Outlook & summary
Advantages
Emittance exchange (in general) for horizontal kicker-bump injection has several advantages
  Less horizontal dynamic aperture required
  Relaxation of e.g. septum blade thickness
  Small bump amplitude needed
Coupling resonance crossing is a simple option
  Readily implementable in modern booster synchrotrons
  “Free”: no extra magnets needed
Challenges
Difficult in high-energy machines with short damping times
Can be harmful with very small vertical apertures in storage ring

## Slide 11: Thank for your attention!
Additional material on emittance exchange by coupling resonance crossing (chronological)
C. Carli and C. Cyvoct, CERN-PS-2001-018, 2001
E. Metral, CERN-PS-2001-066
A. Franchi, E. Metral and R. Tomas, Phys. Rev. Accel. ST Accel. Beams 10, 064003, 2007
P. Kuske and F. Kramer, IPAC’16 proceedings, pp. 2028-2031
J. Kallestrup and M. Aiba, Phys. Rev. Accel. Beams 23, 020701, 2020
M. Aiba and J. Kallestrup, Phys. Rev. Accel. Beams 23, 044003, 2020

## Slide 12: Extra slides

## Slide 13: More on non-adiabatic crossing
Crossing the coupling resonance too quickly will lead to ‘non-adiabatic’ emittance exchange, deteriorating the quality
Non-adiabatic region
If the coupling is small, the crossing speed must be very small
  Increase in a controlled fashion
  Decrease

## Slide 14: and its relation to quantum mechanics
Q.M. : avoided crossing of energy levels
  We can use the same mathematics!
The Landau-Zener formula for probability for non-adiabatic transition in two-level systems:
The Accelerator Physics equivalent:
with
Illu. avoided crossing,
C. Zener, 1932
More on non-adiabatic crossing

## Slide 15: Synchrotron radiation damping
When emittances are out equilibrium, the synchrotron radiation will attempt to restore
  Starts for (for from the beginning)
Beam must be extracted shortly after the exchange
At the same time required for good exchange

## Slide 16: Synchrotron radiation damping
Damping added, fixed extraction
Extraction-point must be optimized to decrease radiative impact