## Slide 1: Status and Development of the ASTRID2 Facility
Jørgen S. Nielsen
(on behalf of the machine group)
Center for Storage Ring Facilities (ISA)
Aarhus University
Denmark

## Slide 2: ASTRID2
ASTRID2 is the “new” synchrotron light source in Aarhus, Denmark, since 2013
ASTRID2 main parameters
  Electron energy: 580 MeV
  Emittance: 12 nm
  Beam Current: 200 mA (presently 180 mA)
  Circumference: 45.7 m
  6-fold symmetry
    lattice: DBA with 12 combined function dipole magnets
      Integrated quadrupole gradient
  4 straight sections for insertion devices
  Using ASTRID as booster (full-energy injection)
      Allows top-up operation

## Slide 3: The ASTRID 2 facility
Microtron (100MeV)
ASTRID2 main parameters
Circumference 45.71m
Energy 580MeV
Current 200mA
Characteristic energy 257eV
RF frequency 105MHz
Harmonic 16
Horiz. emittance 12nmrad
#Straight sections 6
Length of straight sections 2.82m
#ID’s 3
10m
Notes: Microtron, Booster, Inj. Bl., A2 ring, 6 beamlines, 7 experiments

## Slide 4: Corona virus
Denmark was put in lock-down Friday March 13th
After 6 weeks of shutdown, the university slowly opened
  Initially only 3 persons were allowed at our facility
  From June more normal conditions
Partial lock-down again from December 9th
  Now ~3 persons allowed on site (for us)
  So far planned to January 3rd
Almost only local users
  A dozen foreign users (Norway, France, Finland, Spain, Hungary) over the summer
Not really man-power for mail-in
Working on possibilities for remote measurements/experiments

## Slide 5: User hours and reliability
Chart: Availability / MTBF 2018-2020 Corona shutdown 12/3 - 23/4 does not count as availability failure
| 2018 | 2019 | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Availabilty | 0.942 | 0.946 | 0.956 | 0.996 | 1 | 1 | 0.946 | 0.956 | 0.976 | 0.938 | 0.961 | 0.975 | 0.952 | 0.482
MTBF [h] | 57.1 | 97.6 | 80.18 | 145.8 | 133.98 | 79.43 | 107.4 | 48.58 | 71.33 | 54.21 | 63.96 | 105.71 | 108.07 | 27.63
2020 to 15/12 | 0.9358 | 0.9358 | 0.9358 | 0.9358 | 0.9358 | 0.9358 | 0.9358 | 0.9358 | 0.9358 | 0.9358 | 0.9358 | 0.9358
2020 to 15/12 | 88.8 | 88.8 | 88.8 | 88.8 | 88.8 | 88.8 | 88.8 | 88.8 | 88.8 | 88.8 | 88.8 | 88.8
Chart: ASTRID2 User hours
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
User hours | 168.81 | 5038.38 | 5114.46 | 5881.49 | 6249.65 | 6419.64 | 7021.1 | 5678.96
Projected
Downtime: If current goes below 90% of top-up set current
until 15/12
Chart: Failure durations 2018-2020
| 1 | 2 | 5 | 10 | 20 | 50 | 100
2018 | 70 | 11 | 11 | 9 | 5 | 0 | 1
2019 | 26 | 8 | 15 | 11 | 4 | 1 | 2
2020 | 24 | 10 | 4 | 10 | 1 | 1 | 0
MTTR
2018: 2.4 h
2019: 5.7 h
2020 (-Oct): 3.2 h
2020 is until 31/10
Chart: Time between failures 2018 - 2020
| 6 | 24 | 48 | 96 | 168 | 336 | more
2018 | 31 | 22 | 13 | 21 | 16 | 5 | 1
2019 | 15 | 12 | 9 | 9 | 8 | 8 | 6
2020 -Oct | 6 | 12 | 4 | 12 | 4 | 11 | 1
2020 is until 31/10
Notes: User hours estimated per 15/12-20
MTBF 2018 was 52 h

## Slide 6: Failures
2020 were until December a good year (apart from Corona!)
    MTBF: 2018: 57 h, 2019: 98 h, 2020: 91 h (until now)
May: Facility-wide
  Mains failure on a Saturday
  34 h lost because of weekend
Sep.: Microtron
  Failure of modulator HV charge supply
  10 h lost because of weekend
    Also lost some machine development in the following week
Dec.: Microtron
  Water leak in klystron and klystron solenoid magnet
  ~1 week lost
Plus, various smaller issues
Note:
No operator or technician on call during evening and weekends

## Slide 7: Microtron klystron problems
Following some long-time problems with the Microtron klystron, we in October replaced the Microtron klystron (Thomson TH2074A) with our spare (original) klystron
  Had been running about 150.000 hours
  The spare had earlier been used for about 90.000 h (changed 18 years ago)
    Was replaced back then because of unfounded suspicion of a problem
2 weeks ago, the “new” klystron needed more and more drive power (+10 dB in 3 days!)
  More and more power was reflected
    Input cavity detuning
When dismounting, water was found inside the solenoid magnet
  Bottom ~10 cm of klystron had been under water
  Also, a leak in the klystron cooling was found
  Solenoid bottom plate has been sealed (quick fix)
After water leak repair and cleaning, the klystron now again runs very nicely

## Slide 8: Microtron klystron problems 2
Backup plan: Borrow a Thales TH2157A, incl. solenoid from MAX-IV
  Very grateful for the offer
Long-term plan: A new turn-key solid-state modulator and klystron
    3 GHz, ~7.5 MW, ~2 µs pulse length, <10 Hz rep. rate
Water level clearly visible (lead oxides?)
Cleaned
Ready to re-install

## Slide 9: Single Bunch operation
Single Bunch operation in ASTRID2 has now been tested
  Has (always) been a promised beam mode, but since the push from the users has been limited, so far not much priority has been given to the mode
    Small ring (45.7 m) means high revolution frequency (6.559 MHz)
ASTRID: Single Bunch is created by kickout of all other bunches (vertical betatron sideband excitation)
ASTRID2: bunch cleaning is performed during injection bump (horizontal betatron sideband excitation)
Impurities (after one night of running) is smaller than 10-3 (limit of measurement)
1 V/div, 23.4 mA
5 mV/div, 23.4 mA
Reflections (due to imperfect cable termination in scope)
Noise (beam induced excitations) in pickup
Inject 1 multi-bunch train
20 mV/div, 25.7 mA
Notes: Data are from 201117d

## Slide 10: Trying TRIBs
We have tried to introduce Transverse Resonant Island Buckets (TRIBs) in ASTRID2, but so far with no success
  David K. Olsson from MaxLab visited us for one day to help
  Quite easy for us to run near the 3rd (H) and 4th (H and V) order resonances
    The vertical sextupole family is split in 3 power supplies, so we can run the sextupoles asymmetrically
Theoretically (using MatLab AT) it is quite easy to achieve TRIBs
  Hor: 3rd and 4th order using both (some) sextupoles or a (virtual) octupole
  Ver: 4th order using both (some) sextupoles or a (virtual) octupole
  Theoretical the TRIBs are not destroyed by introducing realistic skew quadrupoles
3rd order horizontal
4th order vertical

## Slide 11
Thank you for your attention

## Slide 12: ASTRID2 Layout